## Slide 1
1
OSI MODEL

## Slide 5
2
Introduction

Open Systems Interconnection Basic Reference Model (OSI
Reference Model or OSI Model) is an abstract description for
layered communications and computer network protocol design. It
was developed as part of the Open Systems Interconnection
(OSI) initiative. In its most basic form, it divides network
architecture into seven layers which, from top to bottom, are the
Application, Presentation, Session, Transport, Network, Data-Link,
and Physical Layers. It is therefore often referred to as the OSI
Seven Layer Model.

## Slide 6
3
APPLICATION
PRESENTATION
SESSION
TRANSPORT
NETWORK
DATA LINK
PHYSICAL
APPLICATION
PRESENTATION
SESSION
TRANSPORT
NETWORK
DATA LINK
PHYSICAL
MIDDLE LAYER
MIDDLE LAYER
HIGHER LAYER
HIGHER LAYER
Application to Application
Application to Application
Application to Application
Process to Process
LOWER LAYER
LOWER LAYER
Hop to Hop
Switch
Hop to Hop
Physical Medium
Hub and Repeater
Router
Source to Destination
Source to Destination
OSI Model's
Model's 7
7 Layers
Layers
OSI

## Slide 7
4
Host and Media Layer
and Media Layer
Host

## Slide 8
5
TCP/IP Suit
OSI Layers
Application
Telnet, FTP, SMTP, HTTP, DNS, SNMP, Specific address etc…
Session
Presentation
Transport
SCTP, TCP, UDP, Sockets and Ports address
Network
IP, ARP/RARP, ICMP, IGMP, Logical address
Data Link
IEEE 802 Standards, TR, FDDI, PPP, Physical address
Application
Session
Presentation
Transport
Network
Data Link
Activities
To allow access to network resources
To establish, manage, and terminate
session
To Translate, encrypt, and compress
data
To Provide reliable process-to-process
Message delivery and error recovery
To move packets from source to
destination; to provide internetworking
To organize bits into frames; to provide
Hop-to-hop delivery
Data, Protocol & Activities
& Activities
Data, Protocol
Physical
Medium, Coax, Fiber, 10base, Wireless
Physical
To Transmit bits over a medium; to provide
Mechanical and electrical specifications

## Slide 9
6
Physical Layer

One of the major function of the physical layer is to move data in the form of electromagnetic signals
across a transmission medium.
Its responsible for movements of individual bits from one hop (Node) to next.
Both data and the signals can be either analog or digital.
Transmission media work by conducting energy along a physical path which can be wired or wireless




Concerned:

Physical characteristics of interface and medium (Transmission medium)
Representation of bits (stream of bits (0s or 1s) with no interpretation and encoded into signals)
Data rate (duration of a bit, which is how long it last)
Synchronization of bits (sender and receivers clock must be synchronized)
Line configuration (Point-to-Point, Point-to-Multipoint)
Physical topology
Transmission mode (Simplex, half duplex, full duplex)






10101000000010111
110
From data link layer
10101000000010111
110
To data link layer
Physical layer
Physical layer
Transmission medium

## Slide 10
7
Data Link Layer (Host to Host)

Data link layer is responsible for moving frames from one hop (Node) to the next.

Concerned:

Framing (stream of bits into manageable data units)
Physical addressing (MAC Address)
Flow Control (mechanism for overwhelming the receiver)
Error Control (trailer, retransmission)
Access Control (defining master device in the same link)




Data
H2
T2
From network layer
Data
H2
T2
To network layer
To physical layer
From physical layer
Data link layer
Data link layer

## Slide 11
8
Network Layer (Source to Destination)

The network layer is responsible for the delivery of individual packets from the source
host to the destination host.

Concerned:

Logical addressing (IP Address)
Routing (Source to destination transmission between networks)

Data
H3
Packet
From transport layer
To data link layer
Data
H3
Packet
To transport layer
From data link layer
Network layer
Network layer

## Slide 12
9
Transport Layer (Process to Process)

The transport layer is responsible for the delivery of a message from one process to
another

Concerned:

Service-point addressing (Port address)
Segmentation and reassembly (Sequence number)
Connection control (Connectionless or connection oriented)
Flow control (end to end)
Error Control (Process to Process)




Segments
Data
H4
From session layer
To network layer
Transport layer
Data
H4
Data
H4
Segments
Data
H4
From session layer
From network layer
Transport layer
Data
H4
Data
H4

## Slide 13
10
Session Layer (Dialog initiation)

The session layer is responsible for dialog control and synchronization

Concerned:

Dialog Control (Half Duplex/Full duplex)
Synchronization (Synchronization points, process inline within same page)

Data
H5
From Presentation layer
To transport layer
Data
Data
Syn
Syn
Syn
Data
H5
To Presentation layer
From transport layer
Data
Data
Syn
Syn
Syn
Session layer
Session layer

## Slide 14
11
Presentation Layer (dependency)

The presentation layer is responsible for translation, compression and encryption

Concerned:

Translation (interoperability between different encoding system)
Encryption (Privacy schemes)
Compression (data compression)


Data
H6
From application layer
To session layer
Data
H6
To application layer
From session layer
presentation layer
presentation layer

## Slide 15
12
Data
H7
USER
(Human or Program)
To presentation layer
Data
H7
Application layer
Application layer
Message
Message
Application Layer (user level service)

The application layer is responsible for providing services to the user.

Concerned:

Network virtual terminal (Software)
File transfer, access and management
Mail services
Directory services (access to distributed database sources for global information about various objects



and services)
X.500
FTAM
X.400
X.500
FTAM
X.400
From presentation layer
USER
(Human or Program)