## Slide 1: HDLC HIGH-LEVEL DATA LINK CONTROL PROTOCOL
BY
JOTHIMANI.A
AP/CSE

## Slide 2: HDLC-DEFINITION
High-level Data Link Control (HDLC) is a bit- oriented protocol i.e use bits to stuff flags occurring in data.
HDLC was defined by ISO for use on both point-to-point and multipoint data links.
It supports full-duplex communication i.e receive and transmit at the same time.
ITU modified HDLC for use in X.25 network interface and called it Balanced Link Access Protocol (LAPB)
Other similar protocols are
  Synchronous Data Link Control (SDLC) by IBM
  Advanced Data Communication Control Procedure
(ADCCP) by ANSI

## Slide 3: HDLC-FEATURES
Reliable protocol
  selective repeat or go-back-N
Full-duplex communication
  receive and transmit at the same time
  Bit-oriented protocol
  use bits to stuff flags occurring in data . i.e, it does NOT recognize or interpret byte value
Flow control
  adjust window size based on receiver capability
Uses physical layer clocking and synchronization to send and receive frames

## Slide 4: HDLC-OVERVIEW
Defines three types of stations
  Primary
  Secondary
  Combined
Defines three types of data transfer mode
  Normal Response mode
  Asynchronous Response mode
  Asynchronous Balanced mode
Three types of frames
  Unnumbered
  information
  Supervisory

## Slide 5: HDLC STATIONS
The three stations are :
  Primary station
    Has the responsibility of controlling the operation of data flow .
    Handles error recovery
    Frames issued by the primary station are called commands.
  Secondary station,
    Operates under the control of the primary station.
    Frames issued by a secondary station are called responses.
    The primary station maintains a separate logical link with each secondary station.
  Combined station,
    Acts as both as primary and secondary station

## Slide 6: THREE TRANSFER MODES
1. NORMAL RESPONSE MODE(NRM)
2. ASYNCHRONOUS RESPONSE MODE(ARM)
3. ASYNCHRONOUS BALANCE MODE (ABM)
The three modes of data transfer operations are
  Normal Response Mode (NRM)
    Secondary station can send ONLY when the primary station instruct it to do so
    Two common configurations
      Point-to-Point link (one primary station and one secondary station)
      Multipoint link (the primary station maintain different sessions with different secondary stations)
  Asynchronous Response Mode (ARM)
  More independent secondary station
  Can send data or control information without explicit permission to do so (note that it is still can not send commands)
  Asynchronous Balanced Mode (ABM)
    Mainly used in point-to-point links, for communication between combined stations
    Either stations can send data, control information and commands

## Slide 7: CONTD..

## Slide 8: HDLC FRAME & CONTROL FIELD FORMAT

## Slide 9: HDLC THREE FRAMES
Unnumbered frames (U-frames) :- These frames are used in link set-up and disconnection.
Information frames (I-frames) :-
These frames carry the actual information.
Supervisory frames (S-frames) :-
S-frames are used only to transport control information
Flag: 01111110- indicates start and ending of frames
FCS: 16-bit CRC using generating polynomial
G(x) = x16 + x12 + x5 + 1
Address field:
  When a primary station is sending a frame, the address field contains the receiver identity
  If a secondary station is sending the frame, the address field
contains the sender identity

## Slide 10: CONTD.
  In some cases, it contains a group or broadcast address
In I-frames, N(s) is the sequence number of the frame being sent, and N(r) is the sequence number of the frame being expected.
The P/F bit, known as the poll/final bit, is used with different meaning in different contexts.
It is used to indicate polling, to indicate the final I-frame, etc
There are four different supervisory frames
  SS=00, Receiver Ready (RR), and N(R) ACKs all frames received up to and including the one with sequence number N(R) - 1
  SS=10, Receiver Not Ready (RNR), and N(R) has the same meaning as above
  SS=01, Reject; all frames with sequence number N(R) or higher are rejected, which in turns ACKs frames with sequence number N(R) -1 or lower.
  SS=11, Selective Reject; the receive rejects the frame with
sequence number N(R)

## Slide 11
The unnumbered frames can be grouped into the following categories:
  Mode-setting commands and responses
  Recovery commends and responses
  Miscellaneous commands and responses