## Slide 1
Course Learning Rationale
Course Learning Outcomes
Emphasize the importance of Memory Management concepts of an Operating system
Understand the need of Memory Management functions of an Operating system
UNIT 3 Memory Management

## Slide 2: Topics
1 | MEMORY MANAGEMENT: Memory Management: Logical Vs Physical address space, Swapping
 | Understanding the basics of Memory management
2 | Contiguous Memory allocation – Fixed and Dynamic partition
 | Getting to know about Partition memory management and issues: Internal fragmentation and external fragmentation problems
3 | Strategies for selecting free holes in Dynamic partition
 | Understanding the allocation strategies with examples
4 | Paged memory management
 | Understanding the Paging technique.PMT hardware mechanism
5 | Structure of Page Map Table
 | Understanding the components of PMT
6 | Example : Intel 32 bit and 64 –bit Architectures
 | Understanding the Paging in the Intel architectures
7 | Example : ARM Architectures
 | Understanding the Paging with respect to ARM
8 | Segmented memory management
 | Understanding the users view of memory with respect to the primary memory
9 | Paged segmentation Technique
 | Understanding the combined scheme for efficient management

## Slide 3: Basics of Memory Management

## Slide 4: Memory : Basics
Memory is central part for the operation of a modern computer system
Memory consists of a large array of words or bytes, each with its own address.
The CPU fetches instructions from memory according to the value of the program counter which may need additional loading from and storing to specific memory addresses.
A typical instruction-execution cycle, first fetches an instruction from memory. The instruction is then decoded and may cause operands to be fetched from memory.
After the instruction has been executed on the operands, results may be stored back in memory.
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 5: Memory : Basics (Cont.)
The memory unit sees only a
  Stream of memory addresses;
  It does not know how they are generated (by the instruction counter, indexing, indirection, literal addresses, and so on) or
  What they are for (instructions or data).
Hence we can ignore how a program generates a memory address.
We are interested only in the sequence of memory addresses generated by the running program.
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 6: Basic Hardware
Program must be brought (from disk) into memory and placed within a process for it to be run
Main memory and registers are only storage CPU can access directly
Memory unit only sees a stream of addresses + read requests, or address + data and write requests
Register access in one CPU clock (or less)
Main memory can take many cycles, causing a stall Cache sits between main memory and CPU registers
Protection of memory required to ensure correct operation
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 7: A Base and a Limit Register
Each process should have a separate memory space.
To do this, we need the ability to determine the range of legal addresses that the process may access and to ensure that the process can access only these legal addresses.
Operating system provide this protection by using two registers:
  a base and
  a limit
The base register holds the smallest legal physical memory address
The limit register specifies the size of the range
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 8: A Base and a Limit Register
For example, if the base register holds 300040 and
The limit register is 120900, then the program can legally access all addresses from 300040 through 420939 (inclusive).
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 9: Hardware Address Protection
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 10: Address Binding
Usually, a program resides on a disk as a binary executable file.
The program to be executed must be brought into memory and placed within a process.
Depending on the memory management in use, the process may be moved between disk and memory during its execution.
The processes on the disk that are waiting to be brought into memory for execution form the input queue.
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 11: Address Binding
Addresses may be represented in different ways during the execution of the program
Addresses in the source program are generally symbolic (such as count)
A compiler will typically bind these symbolic addresses to relocatable addresses (such as “14 bytes from the beginning of this module”)
The linkage editor or loader will in turn bind the relocatable addresses to absolute addresses (such as 74014)
Each binding is a mapping from one address space to another.
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 12: Binding of Instructions and Data to Memory
Address binding of instructions and data to memory
addresses can happen at three different stages
  Compile time: If memory location known a priori, absolute code can be generated; must recompile code if starting location changes
  Load time: Must generate relocatable code if memory location is not known at compile time
  Execution time: Binding delayed until run time if the process can be moved during its execution from one memory segment to another
    Need hardware support for address maps (e.g., base and limit registers)
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 13: Multistep Processing of a User Program
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 14: Program Execution

## Slide 15: Compilation
Source Code
Compiled code

## Slide 16: Assembler
Assembly Code

## Slide 18: Linker/Loader
Machine Code

## Slide 19: Logical vs Physical Address Space
An address generated by the CPU is commonly referred to as a logical address
An address seen by the memory unit—that is, the one loaded into the memory-address register of the memory—is commonly referred to as a physical address.
The compile-time and load-time address-binding methods generate identical logical and physical addresses.
However, the execution-time address binding scheme results in differing logical and physical addresses.
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 20: Logical vs Physical Address Space (Cont.)
In this case, we usually refer to the logical address as a virtual address.
The set of all logical addresses generated by a program is a logical address space;
The set of all physical addresses corresponding to these logical addresses is a physical address space.
The run-time mapping from virtual to physical addresses is done by a hardware device called the memory-management unit (MMU).
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 21: Dynamic Relocation using a Relocation Register
The base register is now called a Relocation Register.
The value in the relocation register is added to every address generated by a user process at the time the address is sent to memory.
For example, if the base is at 14000, then an attempt by the user to address location 0 is dynamically relocated to location 14000;
an access to location 346 is mapped to location 14346.
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 22
The two different types of addresses:
  logical addresses (in the range 0 to max) and
  physical addresses (in the range R + 0 to R + max for a base value R)
The user generates only logical addresses and thinks that the process runs in locations 0 to max.
The user program generates only logical addresses and thinks that the process runs in locations 0 to max.
However, these logical addresses must be mapped to physical addresses before they are used.
Logical vs Physical Address Space (Cont.)
Courtesy : Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013

## Slide 23: Dynamic Loading

## Slide 24: Dynamic linking
  Static linking
  System libraries and program code seperately
  Some OS support only static linking
Dynamic linking
  Linking is postponed until execution time
  Wastage of both disk space and main memory is avoided

## Slide 25: Swapping
A process can be swapped temporarily out of memory to a backing store, and then brought back into memory for continued execution
  Total physical memory space of processes can exceed physical memory
  This increases the degree of multiprogramming in a system
    Backing store – Normally its hard disk

## Slide 26: CONTIGUOUS MEMORY ALLOCATION

## Slide 27: Contiguous Allocation
The main memory must accommodate both the operating system and the various user processes.
The memory is usually divided into two partitions:
  one for the resident operating system
  one for the user processes.

## Slide 28: Contiguous Allocation (Cont.)
Several user processes want to reside in memory at the same time.
Then it is to be considered, how to allocate available memory to the processes that are in the input queue waiting to be brought into memory.
In contiguous memory allocation, each process is contained in a single section of memory that is contiguous to the section containing the next process.

## Slide 29: Contiguous Allocation (Cont.)
The relocation register contains the value of the smallest physical address;
The limit register contains the range of logical addresses (for example, relocation = 100040 and limit = 74600).
Each logical address must fall within the range specified by the limit register.
The MMU maps the logical address dynamically by adding the value in the relocation register.

## Slide 30: Contiguous Allocation (Cont.)
This mapped address is sent to memory. When the CPU scheduler selects a process for execution, the dispatcher loads the relocation and limit registers with the correct values as part of the context switch.
Because every address generated by a CPU is checked against these registers, we can protect both the operating system and the other users programs and data from being modified by this running process.

## Slide 31: Hardware Support for Relocation and Limit Registers

## Slide 32: Contiguous Allocation (Cont.)
The relocation-register scheme provides an effective way to allow the operating system’s size to change dynamically. This flexibility is desirable in many situations.
For example, the operating system contains code and buffer space for device drivers.

## Slide 33: Contiguous Allocation (Cont.)
If a device driver (or other operating-system service) is not commonly used, we do not want to keep the code and data in memory, as we might be able to use that space for other purposes.
Such code is sometimes called transient operating-system code; it comes and goes as needed. Thus, using this code changes the size of the operating system during program execution.

## Slide 34: Contiguous Allocation Technique
There are two popular techniques used for contiguous memory allocation
      Fixed Partitioning
      Variable Partitioning

## Slide 35: Fixed Partitioning
Static partitioning is a fixed partitioning scheme.
In this partitioning, number of partitions (non-overlapping) in RAM are fixed but size of each partition may or may not be same.
As it is contiguous allocation, hence no spanning is allowed.
Here partition are made before execution or during system configure.
Each partition is allowed to store only one process.
These partitions are allocated to the processes as they arrive.

## Slide 36: Fixed Partitioning (Cont.)
The degree of multiprogramming is bound by the number of partitions.
In this multiple partition method, when a partition is free, a process is selected from the input queue and is loaded into the free partition.
When the process terminates, the partition becomes available for another process.

## Slide 37: Fixed Partitioning (Cont.)
Example

## Slide 38: Disadvantages of Fixed Partitioning
Limitation on the Size of the Process: – Sometimes, when the size of the process is larger than the maximum partition size, then we cannot load that process into the memory. So, this is the main disadvantage of the fixed partition.
Degree of Multiprogramming is Less: – We can understand from the degree of multiprogramming that it means at the same time, the maximum number of processes we can load into the memory. In Fixed Partitioning, the size of the partition is fixed, and we cannot vary it according to the process size; therefore, in fixed partitioning, the degree of multiprogramming is less and fixed.
Internal Fragmentation
Let us first discuss about what is fragmentation and then discuss about Internal Fragmentation

## Slide 39: Fragmentation
Fragmentation is an unwanted problem where the memory blocks cannot be allocated to the processes due to their small size and the blocks remain unused.
It can also be understood as when the processes are loaded and removed from the memory they create free space or hole in the memory and these small blocks cannot be allocated to new upcoming processes and results in inefficient use of memory.
Basically, there are two types of fragmentation:
    Internal Fragmentation
    External Fragmentation

## Slide 40: Internal Fragmentation
It occurs when the space is left inside the partition after allocating the partition to a process.
This space is called as internally fragmented space.
This space can not be allocated to any other process.
This is because only Fixed (static) partitioning allows to store only one process in each partition.
Internal Fragmentation occurs only in Fixed (static) partitioning .

## Slide 41: Internal Fragmentation (Cont.)

## Slide 42
This problem is occurring because we have fixed the sizes of the memory blocks. This problem can be removed if we use dynamic partitioning for allocating space to the process.
In dynamic partitioning, the process is allocated only that much amount of space which is required by the process. So, there is no internal fragmentation.
Solution to Internal Fragmentation

## Slide 43: Variable - Partitioning
In the variable-partition scheme, the operating system keeps a table indicating which parts of memory are available and which are occupied.
Initially, all memory is available for user processes and is considered one large block of available memory, a hole.
Eventually, memory contains a set of holes of various sizes.
As processes enter the system, they are put into an input queue.

## Slide 44: Variable – Partitioning (Cont.)

## Slide 45: Variable – Partitioning (Cont.)
The operating system takes into account the memory requirements of each process and the amount of available memory space in determining which processes are allocated memory.
When a process is allocated space, it is loaded into memory, and it can then compete for CPU time.
When a process terminates, it releases its memory, which the operating system may then fill with another process from the input queue.

## Slide 46: Variable – Partitioning (Cont.)
At any given time, then, we have a list of available block sizes and an input queue. The operating system can order the input queue according to a scheduling algorithm. Memory is allocated to processes until, finally, the memory requirements of the next process cannot be satisfied — that is, no available block of memory (or hole) is large enough to hold that process.

## Slide 47: Variable – Partitioning (Cont.)
The operating system can then wait until a large enough block is available, or it can skip down the input queue to see whether the smaller memory requirements of some other process can be met.
In general, as mentioned, the memory blocks available comprise a set of holes of various sizes scattered throughout memory. When a process arrives and needs memory, the system searches the set for a hole that is large enough for this process.

## Slide 48: Variable – Partitioning (Cont.)
If the hole is too large, it is split into two parts. One part is allocated to the arriving process; the other is returned to the set of holes.
When a process terminates, it releases its block of memory, which is then placed back in the set of holes.
If the new hole is adjacent to other holes, these adjacent holes are merged to form one larger hole.
At this point, the system may need to check whether there are processes waiting for memory and whether this newly freed and recombined memory could satisfy the demands of any of these waiting processes.

## Slide 49: Variable – Partitioning (Cont.)

## Slide 50: Variable – Partitioning (Cont.)
This procedure is a particular instance of the general dynamic storage-allocation problem, which concerns how to satisfy a request of size n from a list of free holes.
There are many solutions to this problem. The first-fit, best-fit, and worst-fit strategies are the ones most commonly used to select a free hole from the set of available holes.

## Slide 51: Partition Allocation Algorithm

## Slide 52: First Fit
Allocate the first hole that is big enough.
Searching can start either at the beginning of the set of holes or at the location where the previous first-fit search ended.
We can stop searching as soon as we find a free hole that is large enough.

## Slide 53: Best Fit
Allocate the smallest hole that is big enough.
We must search the entire list, unless the list is ordered by size.
This strategy produces the smallest leftover hole.

## Slide 54: Worst Fit
Allocate the largest hole.
Again, we must search the entire list, unless it is sorted by size.
This strategy produces the largest leftover hole which may be useful for the other process

## Slide 55: Problem to Solve
Question
Given five memory partitions of 100Kb, 500Kb, 200Kb, 300Kb, 600Kb (in order), how would the first-fit, best-fit, and worst-fit algorithms place processes of 212 Kb, 417 Kb, 112 Kb, and 426 Kb (in order)? Which algorithm makes the most efficient use of memory?

## Slide 56: Steps to Solve – First Fit

## Slide 57: Steps to Solve – Best Fit

## Slide 58: Steps to Solve – Worst Fit

## Slide 59: Disadvantages of Variable - Partitioning
Complex Memory Allocation
External Fragmentation

## Slide 60: Complex Memory Allocation
The task of allocation and deallocation is tough because the size of the partition varies whenever the partition is allocated to the new process. The operating system has to keep track of each of the partitions.
So, due to the difficulty of allocation and deallocation in the dynamic memory allocation, and every time we have to change the size of the partition; therefore, it is tough for the operating system to handle everything.

## Slide 61: External Fragmentation
It occurs when the total amount of empty space required to store the process is available in the main memory.
But because the space is not contiguous, so the process can not be stored.

## Slide 62: External Fragmentation (Cont.)
Consider, three processes P1 (1MB), P2 (3MB), and P3 (1MB), and we want to load the processes in the various partitions of the main memory.
Now the processes P1 and P3 are completed, and space that is assigned to the process P1 and P3 is freed. Now we have partitions of 1 MB each, which are unused and present in the main memory, but we cannot use this space to load the process of 2 MB in the memory because space is not contiguous.
The rule says that we can load the process into the memory only when it is contiguously residing in the main memory. So, if we want to avoid external fragmentation, then we have to change this rule.

## Slide 63: External Fragmentation (Cont.)
Example

## Slide 64: Solution to External Fragmentation
This problem is occurring because we are allocating memory continuously to the processes. So, if we remove this condition external fragmentation can be reduced.
One of the way to remove external fragmentation is compaction. When dynamic partitioning is used for memory allocation then external fragmentation can be reduced by merging all the free memory together in one large block.

## Slide 65: Solution to External Fragmentation (Cont.)

## Slide 66: Solution to External Fragmentation (Cont.)
This technique is also called defragmentation. This larger block of memory is then used for allocating space according to the needs of the new processes.
Problem with Compaction
Due to compaction, the system efficiency is decreased because we need to move all the free spaces from one place to other.
In this way, the more amount of time is wasted, and the CPU remains ideal all the time. Instead of that, with the help of compaction, we can avoid external fragmentation, but this will make the system inefficient.

## Slide 67: Solution to External Fragmentation (Cont.)
Another way, paging & segmentation (non-contiguous memory allocation techniques) where memory is allocated non-contiguously to the processes.

## Slide 68: Fixed vs Variable Partitioning
S.NO. | Fixed partitioning | Variable partitioning
1. | In multi-programming with fixed partitioning the main memory is divided into fixed sized partitions. | In multi-programming with variable partitioning the main memory is not divided into fixed sized partitions.
2. | Only one process can be placed in a partition. | In variable partitioning, the process is allocated a chunk of free memory.
3. | It does not utilize the main memory effectively. | It utilizes the main memory effectively.
4. | There is presence of internal fragmentation and external fragmentation. | There is external fragmentation.
5. | Degree of multi-programming is less. | Degree of multi-programming is higher.
6. | It is more easier to implement. | It is less easier to implement.
7. | There is limitation on size of process. | There is no limitation on size of process.

## Slide 69: Internal vs External Fragmentation
INTERNAL FRAGMENTATION | EXTERNAL FRAGMENTATION
Memory allocated to a process may be slightly larger than the requested memory. The difference between these two numbers is internal fragmentation. | External fragmentation exists when there is enough total memory space to satisfy a request but available spaces are not contiguous.
First-fit and best-fit memory allocation does not suffer from internal fragmentation. | First-fit and best-fit memory allocation suffers from external fragmentation.
Systems with fixed-sized allocation units, such as the single partitions scheme and paging suffer from internal fragmentation. | Systems with variable-sized allocation units, such as the multiple partitions scheme and segmentation suffer from external fragmentation.

## Slide 70: Non Contiguous Allocation
Non-contiguous memory allocation is a memory allocation technique.
It allows to store parts of a single process in a non-contiguous fashion.
Thus, different parts of the same process can be stored at different places in the main memory.

## Slide 71: Techniques

## Slide 72: PAGING

## Slide 73: Paging
Paging is a memory management scheme that eliminates the need for contiguous allocation of physical memory.
Paging permits the physical address space of a process to be non – contiguous.
The mapping from virtual to physical address is done by the memory management unit (MMU) which is a hardware device and this mapping is known as paging technique.

## Slide 74: Example
Consider a process is divided into 4 pages P0, P1, P2 and P3.

## Slide 75
In the above example, the process P is divided into 4 sections namely P0, P1, P2, P3.
All the four sections are mapped in the main memory in a non – contiguous fashion.

## Slide 76: Paging
In the paging mechanism two addresses are involved
Logical Address
  CPU always generates a logical address.
Physical Address
  A physical address is needed to access the main memory.

## Slide 77: Logical Address and Physical Address
Logical Address or Virtual Address :
An address generated by the CPU
Logical Address Space or Virtual Address Space:
The set of all logical addresses generated by a program
Physical Address:
An address actually available on memory unit
Physical Address Space :
The set of all physical addresses corresponding to the logical addresses

## Slide 78
The Physical Address Space is conceptually divided into a number of fixed-size blocks, called frames.
The Logical address Space is also divided into fixed-size blocks, called pages.
Page Size = Frame Size

## Slide 79: Logical Address
Address generated by CPU is divided into:
  Page number (p) – used as an index into a page table which contains base address of each page in physical memory
  Page offset (d) – combined with base address to define the physical memory address that is sent to the memory unit
  For given logical address space 2m and page size 2n

## Slide 80: Physical Address
Physical Address is divided into
Frame number(f): Number of bits required to represent the frame of Physical Address Space or Frame number.
Frame offset(d): Number of bits required to represent particular word in a frame or frame size of Physical Address Space or word number of a frame or frame offset.

## Slide 81
If Logical Address = 31 bit, then Logical Address Space = 231 words = 2 G words (1 G = 230)
If Logical Address Space = 128 M words = 27 * 220 words, then Logical Address = log2 227 = 27 bits
If Physical Address = 22 bit, then Physical Address Space = 222 words = 4 M words (1 M = 220)
If Physical Address Space = 16 M words = 24 * 220 words, then Physical Address = log2 224 = 24 bits

## Slide 82: Memory Management
The Mapping between these two address is done to execute the process using the paging technique.
The Hardware device that at run time maps virtual address to physical address is done by the Memory Management Unit (MMU)

## Slide 85: Paging Hardware
How does system perform translation? Simplest solution: use a page table.
Page table is a linear array indexed by virtual page number that gives the physical page frame that contains that page through the look up process.

## Slide 86: Paging Hardware

## Slide 87: Paging Hardware
LOOK UP PROCESS
Step 1 :Extract page number.
Step 2 : Extract offset.
Step 3 : Check that page number is within address space of process.
Step 4 : Look up page number in page table.
Step 5 : Add offset to resulting physical page number
Step 6 : Access memory location.

## Slide 88: Paging Model of Logical and Physical Memory

## Slide 89
In the example a process is divided into four pages as page0, page1, page 2 and page3.
All the four pages are mapped to the frames in the physical memory through the page table.
The page table maps the page number to its corresponding frame number in the physical memory.
page0 is mapped to frame1 , page1 is mapped to frame 4, page2 is mapped to frame 3 and page4 is mapped to frame 7.

## Slide 90: Paging Example

## Slide 91: Free Frame List

## Slide 92: Free Frame List
The example
Fig (a) shows a process divided into 4 pages and the list of free frames available in the physical memory.
Fig(b) shows the mapping of these pages to the free frames available and the updated list of free frames available in the physical memory.

## Slide 93: Page Table
Page table is kept in main memory
Page-table base register (PTBR) points to the page table
Page-table length register (PTLR) indicates size of the page table

## Slide 95: Problem with paging
In this scheme every data/instruction access requires two memory accesses
  One for the page table and one for the data / instruction
The two memory access problem can be solved by the use of a special fast-lookup hardware cache called associative memory or translation look-aside buffers (TLBs)

## Slide 97: Translation Lookaside Buffer (TLB)
Speed up the lookup problem with a cache. Store most recent page lookup values in TLB.
Procedure of TLB
Step 1 :Extract page number.
Step 2 : Extract offset.
Step 3 : Look up page number in TLB.
Step 4 : If there, add offset to physical page number and access memory location.
Step 5 : Otherwise, trap to OS. OS performs check, looks up physical page number, and loads translation into TLB. Restarts the instruction.

## Slide 98: Paging with TLB

## Slide 99
If the page number is not in the TLB (TLB miss) a memory reference to the page table must be made.
In addition, we add the page number and frame number into TLB
If the TLB already full, the OS have to must select one for replacement
Some TLBs allow entries to be wire down, meaning that they cannot be removed from the TLB, for example kernel codes
The percentage of times that a particular page number is found in the TLN is called hit ratio

## Slide 100
Fixed size allocation of physical memory in page frames dramatically simplifies allocation algorithm.
OS can just keep track of free and used pages and allocate free pages when a process needs memory.
There is no fragmentation of physical memory into smaller and smaller allocatable chunks.

## Slide 101: Effective Access Time
Associative Lookup = ε time unit
  Can be < 10% of memory access time
Hit ratio = α
  Hit ratio – percentage of times that a page number is found in the associative registers; ratio related to number of associative registers
Consider α = 80%, ε = 20ns for TLB search, 100ns for memory access
Effective Access Time (EAT)
EAT = (1 + ε) α + (2 + ε)(1 – α)
= 2 + ε – α
Consider α = 80%, ε = 20ns for TLB search, 100ns for memory access
  EAT = 0.80 x 100 + 0.20 x 200 = 120ns

## Slide 102: Memory Protection
The process has to be protected for the following reasons:
  Preventing one process from reading or writing another process' memory.
  Preventing one process from reading another process' memory.
  Preventing a process from reading or writing some of its own memory.
  Preventing a process from reading some of its own memory.

## Slide 103: Memory Protection
Memory protection is implemented by associating protection bit with each frame to indicate if read-only or read-write access is allowed
  Can also add more bits to indicate page execute-only, and so on
Valid-invalid bit attached to each entry in the page table:
  “valid” indicates that the associated page is in the process’ logical address space, and is thus a legal page
  “invalid” indicates that the page is not in the process’ logical address space
  Or use page-table length register (PTLR)
Any violations result in a trap to the kernel

## Slide 104: Valid – Invalid Bit

## Slide 105
Pages that are not loaded into memory are marked as invalid in the page table, using the invalid bit.
In the above example Page0 to page5 is present in the memory .so , the corresponding valid/Invalid bit is marked as V(Valid).
The other pages which are not loaded such as page6 and page7 are marked as I(Invalid)

## Slide 106: PageFault
if a page is needed that was not originally loaded up, then a page fault trap is generated
Page fault is handled by the following steps:
Step 1: The memory address requested is first checked, to make sure it was a valid memory request.
Step 2: If the reference was invalid, the process is terminated. Otherwise, the page must be paged in.
Step 3: A free frame is located, possibly from a free-frame list.

## Slide 107
Step 4: A disk operation is scheduled to bring in the necessary page from disk.
Step 5: When the I/O operation is complete, the process's page table is updated with the new frame number, and the invalid bit is changed to indicate that this is now a valid page reference.
Step 6: The instruction that caused the page fault must now be restarted from the beginning

## Slide 109: Shared Pages
Shared code
  One copy of read-only (reentrant) code shared among processes (i.e., text editors, compilers, window systems)
  Similar to multiple threads sharing the same process space
  Also useful for interprocess communication if sharing of read-write pages is allowed
Private code and data
  Each process keeps a separate copy of the code and data
  The pages for the private code and data can appear anywhere in the logical address space

## Slide 110: Shared Pages

## Slide 111: Shared Pages
In the example figure, three pages ed1,ed2 and ed3 are shred by three processes Process1 , Process2, Process3.
The page is loaded only once and the corresponding frame number is updated in the page table of the three processes.

## Slide 112: STRUCTURE OF A PAGE TABLE

## Slide 113: Structure of the Page Table
Memory structures for paging can get huge using straight-forward methods
  Consider a 32-bit logical address space as on modern computers
  Page size of 4 KB (212)
  Page table would have 1 million entries (232 / 212)
  If each entry is 4 bytes -> 4 MB of physical address space / memory for page table alone
    That amount of memory used to cost a lot
    Don’t want to allocate that contiguously in main memory
Hierarchical Paging
Hashed Page Tables
Inverted Page Tables

## Slide 114: Two-Level Paging Example
Simple solution to this problem is to divide the page table into smaller pieces We can accomplish this division in several ways
A logical address (on 32-bit machine with 1K page size) is divided into:
  a page number consisting of 22 bits
  a page offset consisting of 10 bits
Since the page table is paged, the page number is further divided into:
  a 12-bit page number
  a 10-bit page offset
Thus, a logical address is as follows:
where p1 is an index into the outer page table, and p2 is the displacement within the page of the inner page table
Known as forward-mapped page table

## Slide 115: Hierarchical Page Tables
Break up the logical address space into multiple page tables
A simple technique is a two-level page table
We then page the page table

## Slide 116: Two-Level Page-Table Scheme

## Slide 117: Address-Translation Scheme for two level 32 bit paging architecture

## Slide 118: 64-bit Logical Address Space
For a system with a 64-bit logical address space, a two-level paging scheme is no longer appropriate
If page size is 4 KB (212)
  Then page table has 252 entries
  If two level scheme, inner page tables could be 210 4-byte entries
  Address would look like
  Outer page table has 242 entries or 244 bytes
  One solution is to add a 2nd outer page table
  But in the following example the 2nd outer page table is still 234 bytes in size
    And possibly 4 memory access to get to one physical memory location

## Slide 119
We can divide the outer page table in various ways. For example, we can page the outer page table, giving us a three-level paging scheme. Suppose that the outer page table is made up of standard-size pages (210 entries, or 212 bytes). In this case, a 64-bit address space is still daunting
This keeps growing that is the reason hierarchical page tables are generally considered inappropriate

## Slide 120: Three-level Paging Scheme

## Slide 121: Hashed Page Tables
One approach for handling address spaces larger than 32 bits is to use a hashed page table, with the hash value being the virtual page number
Common in address spaces > 32 bits
The virtual page number is hashed into a page table
  This page table contains a chain of elements hashing to the same location
Each element contains (1) the virtual page number (2) the value of the mapped page frame (3) a pointer to the next element

## Slide 122: Hashed Page Tables (Cont.)
Virtual page numbers are compared in this chain searching for a match
  If a match is found, the corresponding physical frame is extracted
Variation for 64-bit addresses is clustered page tables
  Similar to hashed but each entry refers to several pages (such as 16) rather than 1
  Especially useful for sparse address spaces (where memory references are non-contiguous and scattered)

## Slide 123: Hashed Page Table

## Slide 124: Inverted Page Table
Rather than each process having a page table and keeping track of all possible logical pages, track all physical pages
One entry for each real page of memory
Entry consists of the virtual address of the page stored in that real memory location, with information about the process that owns that page

## Slide 125: Inverted Page Table Architecture

## Slide 126: Paging - ARM
The paging scheme used by ARM processors uses a 2 level page table.
The first level page table has 16kB size and each entry covers a region of 1MB (sections).
The second level page tables have 1kB size and each entry covers a region of 4KB (pages).
The TLB also supports 16MB sections and 64kB pages

## Slide 127: Paging - ARM
On ARMv4 and ARMv5 pages might also be divided into what the manual calls 'subpages‘
Example : for a 4KB page, 1KB subpages, and for a 64KB page, 16KB subpages.
The ARM processor supports 2 independent page tables.
The first page table can be abbreviated from the full 16kB
The second page table is always 16KB in size and is used for addresses beyond the end of the first page table.

## Slide 129: SEGMENTATION

## Slide 130: Non-Contiguous Memory Allocation
Segmentation

## Slide 131: Segmentation
Memory-management scheme that supports user view of memory.
Segmentation overcomes the problem of dealing with memory in terms of its physical properties which is inconvenient to both the operating system and the programmer.
The system have more freedom to manage memory.
The programmer would get an experience to work in more natural programming environment.

## Slide 132: Program and Segment
A program is a collection of segments in which segment is a logical unit which consists of the following :
      main program
      procedure
      Function
      Method
      Object
      local variables, global variables
      common block
      Stack
      symbol table
      arrays

## Slide 133: User’s View of a Program
Most programmers prefer to view memory as a collection of variable-sized segments with no necessary ordering among the segments.
From programmer point of view , a program will appear as a main program with a set of methods, procedures, or functions. Program also includes the following data structures:
  Objects
  Arrays
  Stacks and
  Variables
Modules or data elements is referred by name.
The programmer talks about “the stack,” “the math library,” and “the main program” without caring what addresses in memory these elements occupy.
Programmer is not concerned with whether the stack is stored before or after the Sqrt() function.

## Slide 134: Logical View of Segmentation
1
3
2
4
1
4
2
3
user space
physical memory space
In the figure, both user space and physical memory space are given.
Segments vary in length, and the length of each is intrinsically defined by its purpose in the program.
Segments are numbered as 1,2,3 and 4.
In Physical memory space, Segments are allocated in different parts of the memory
For example,
  Elements within a segment are identified by their offset from the beginning of the segment: the first statement of the program, the seventh stack frame entry in the stack and the fifth instruction of the Sqrt()

## Slide 135: Example – Compilation of C program
Normally, when a program is compiled, the compiler automatically constructs
segments reflecting the input program.
A “C” compiler might create separate segments for the following:
  The code
  Global variables
  The heap, from which memory is allocated
  The stacks used by each thread
  The standard C library
Libraries that are linked in during compile time might be assigned separate segments.
The loader would take all these segments and assign them segment numbers.

## Slide 136: Segmentation Architecture
Logical address consists of a two tuple:
<segment-number, offset>
A logical address consists of two parts: a segment number, s, and an offset into that segment, d.
The segment number is used as an index to the segment table.
The offset d of the logical address must be between 0 and the segment limit.
If it is not, a trap is sent to the operating system (logical addressing attempt beyond end of segment).
When an offset d is legal, it is added to the segment base to produce the address in physical memory of the desired byte.

## Slide 137: Segmentation Architecture (Cont.)
Segment table – maps two-dimensional physical addresses; each table entry has:
  base – contains the starting physical address where the segments reside in memory
  limit – specifies the length of the segment
Segment-table base register (STBR) points to the segment table’s location in memory
Segment-table length register (STLR) indicates number of segments used by a program;
segment number s is legal if s < STLR

## Slide 138: Segmentation Architecture (Cont.)
Protection
  With each entry in segment table associate:
    validation bit = 0 ⇒ illegal segment
    read/write/execute privileges
Protection bits associated with segments with code sharing occurs at segment level
Since segments varies in length, memory allocation is a dynamic

## Slide 139: Segmentation Hardware

## Slide 140: Segmentation Example
There are Five Segments numbered from 0 through 4.
The segments are stored in physical memory as shown in the diagram.
The segment table has a separate entry for each segment, giving the beginning address of the segment in physical memory (or base) and the length of that segment (or limit).
For example, segment 2 is 400 bytes long and begins at location 4300.
A reference to byte 53 of segment 2 is mapped onto location 4300 + 53 = 4353.
A reference to segment 3, byte 852, is mapped to 3200 (the base of segment 3) + 852 = 4052.
A reference to byte 1222 of segment 0 would result in a trap to the operating system, as this segment is only 1,000 bytes long.

## Slide 141: Paged Segmentation
Paging + Segmentation
Takes advantage of both paging and segmentation
Implementation: Treat each segment independently. Each segment has a page table
Logical address now consists of 3 parts:
  Segment number
  Page number
  Offset

## Slide 142: Paged Segmentation Implementation
Segment table has base address for page table
Look up <page number, offset> in page table
Get physical address in return
Examples: MULTICS and Intel 386

## Slide 143: Combined Paging and Segmentation Scheme
In a combined paging/segmentation system, a user’s address is broken up into a number of segments.
Each segment is broken up into a number of fixed-sized pages which are equal in length to the main memory frame

## Slide 144: Address Translation

## Slide 145: Advantages of Combined Scheme
Reduces memory usage as opposed to pure paging
  Page table size limited by segment size
  Segment table has only one entry per actual segment
Share individual pages by copying page table entries
Share whole segments by sharing segment table entries, which is the same as sharing the page table for that segment
Most advantages of paging still hold
  Simplifies memory allocation
  Eliminates external fragmentation
This system combines the efficiency in paging with protection and sharing capabilities of segmentation

## Slide 146: Disadvantage
Internal fragmentation still exists

## Slide 147: Example: The Intel 32 and 64-bit Architectures
Dominant industry chips
Pentium CPUs are 32-bit and called IA-32 architecture
Current Intel CPUs are 64-bit and called IA-64 architecture
Many variations in the chips, cover the main ideas here

## Slide 148: Example: The Intel IA-32 Architecture
Memory management is divided as – Segmentation and Paging
CPU generates logical address
  Selector given to segmentation unit
    Which produces linear addresses
  Linear address given to paging unit
    Which generates physical address in main memory
    Paging units form equivalent of MMU
    Pages sizes can be 4 KB or 4 MB

## Slide 149: The Intel IA-32 Segmentation
Supports both segmentation and paging
  Each segment can be 4 GB
  Up to 16 K segments per process
  Divided into two partitions
    First partition of up to 8 K segments are private to process (kept in local descriptor table (LDT))
    Second partition of up to 8K segments shared among all processes (kept in global descriptor table (GDT))

## Slide 150: Intel IA-32 Segmentation
The logical address is a pair (selector, offset), where the selector is a 16-bit number:
s designates segment number
g indicates if segment is GDT or LDT
p deals with protection
Offset is a 32-bit number and it specifies the location of the byte within segment

## Slide 151: Intel IA-32 Segmentation

## Slide 152: Intel IA-32 Segmentation
There are six segment registers – six segments can be addressed at a time
There are six 8-byte microprogram registers to hold LDT or GDT descriptors
Linear address is 32-bits long
  Base and limit of segment is used to generate linear address
  Limit is used to check address validity
  Invalid address results in a trap
  Value of base with offset results in 32-bit address

## Slide 153: IA-32 Paging
Pages sizes of 4KB or 4MB is allowed in IA-32
4KB pages use two-level paging scheme
The 10 higher order bits reference the page directory – outermost page table
The innermost 10 bits refer the inner page table
Lower order 12 bits refer the offset in the page
1 bit in page directory is Page-Size flag
  If set, indicates 4MB page rather than the default 4KB page

## Slide 154: Intel IA-32 Paging Architecture

## Slide 155: Intel IA-32 Page Address Extensions
32-bit address limits led Intel to create page address extension (PAE), allowing 32-bit apps access to more than 4GB of memory space
Paging went to a 3-level scheme
Top two bits refer to a page directory pointer table
Page-directory and page-table entries moved to 64-bits in size
Net effect is increasing address space to 36 bits – 64GB of physical memory
Linux and MAC support PAE
But, 32-bit versions of Windows desktop operating systems still provide support for only 4 GB of physical memory, even if PAE is enabled.

## Slide 156: Intel IA-32 Page Address Extensions

## Slide 157: Intel x86-64
Current generation Intel x86 architecture
Support for larger physical and logical address spaces
64 bit-systems can address 264 of addressable memory (16 exabytes)
In practice, only implement 48 bit addressing
  Page sizes of 4 KB, 2 MB, 1 GB
  Four levels of paging hierarchy
Can also use PAE so virtual addresses are 48 bits and physical addresses are 52 bits

## Slide 158: Reference
Abraham Silberschatz, Peter Baer Galvin, Greg Gagne, Operating systems, 9th ed., John Wiley & Sons, 2013