## Slide 1: BIO-REMEDIATION
TYPES, FACTORS AFFECTING BIOREMEDIATION, ADVANTAGES AND DISADVANTAGES, BIO-AUGMENTATION

## Slide 2: INTRODUCTION
Bioremediation is a microorganism mediated transformation or degradation of contaminants into non-hazardous or less-hazardous substances. Organisms like bacteria, fungi, algae and plants are used
Examples of bioremediation related technologies are phytoremediation, bioventing, bioleaching, land farming, bioreactor, composting, bio augmentation, rhizofiltration and bio stimulation
Recent advancements have also proven successful via the addition of matched microbe strains to the medium to enhance the resident microbe population’s ability to break down contaminants
Microorganisms which help to perform the function of bioremediation are known as bioremediators

## Slide 3: TYPES OF BIOREMEDIATION
There are two types of bioremediation:
In-situ bioremediation
Involves treating the contaminated material at the site
Ex-situ bioremediation
Involves the removal of the contaminated material to be treated elsewhere

## Slide 4: 1.In-situ bioremediation
This involves the treatment of the contamination on-site Eg. Soil contamination
In-situ bioremediation involves the addition of mineral nutrients
These nutrients increase the degradation ability of the microbes that are already present in the soil.
Some cases, new microbes are added to the contamination site
Sometimes, microbes can be genetically engineered microbes were used to degrade contaminants.
Eg. Pseudomonas flurorescens HK44
This approach is based on type of contaminant and type of microbes present in the contaminated site

## Slide 5: a) Bio-venting
This is method of blowing air from the environment into the contaminated soil
First, injection wells must be dug into the contaminated soil, an air blower is used to control the supply of air that is given to the microorganisms
These injection wells can also be used to add nitrogen and phosphorus maximizing the rate of degradation
The dug deep depends on the factors affecting the rate of degradation, type of contamination, soil, nutrient level and concentration of contaminants

## Slide 6: b) Hydrogen peroxide injection
In this method is used when contaminants reached the ground water, bioventing will not be very successful
It functions same as that of bioventing method but hydrogen peroxide is used instead of air blowers to deliver oxygen to the microorganisms
If the soil is shallow, hydrogen peroxide can be administered through sprinkler systems
If the ground water is deep beneath the surface, injection wells are used

## Slide 7: 2. Ex-situ Bioremediation
This involves the physical extraction of the contaminated media to another location for treatment
If the contaminant is soil, it has been excavated and transported for treatment
If contamination has reached the groundwater, it must be pumped and any contaminated soil must also be removed
After excavation some of the minimal contaminants remain in the soil, they can be easily broken down by naturally occurring microbes already present
There are two main types of ex situ bioremediation. They are referred to as phases: a) Solid phase b) slurry phase

## Slide 8: a) Solid phase
This treatment consists of placing the excavated materials into an above ground enclosure
Inside this enclosure, contaminated soil is spread onto a treatment bed which consists of aeration system to control nutrients, moisture, heat, oxygen and pH
This allows them to maximize the efficiency of bioremediation
The contaminated soil can also be tilled like farmland for aerobic biodegradation of contamination
This treatment is especially effective if the contaminants are fuel hydrocarbons
The are three solid phase bioremediation techniques. They are : landfarming, biopiling and composting

## Slide 9: b) Slurry phase
This technique involves contaminated soil is excavated and removed from the site as completely as possible
The contaminants are then put into a large tank which is known as bioreactor
Clean up crews use this bioreactor to mix the contaminants and microorganisms
This mixing process keeps the microbes in constant contact with the contaminants and water, oxygen and nutrients are added during this process
Bioreactor adjust the things until they achieve the optimal conditions for the degradation of the contaminants
Slurry phase bioremediation is faster and permanant than other bioremediation techniques

## Slide 10: Factors determining bioremediation
Types of contamination
Extent of contamination
Toxicity of contaminants
Location and characteristics of site
Economic situation
Microbes (Source of carbon and energy)
Temperature and weather conditions
pH of contaminated site- Bt. 5-10 and optimal pH (6-8)
Moisture content

## Slide 11
Bioremediation cannot be used in cases where the contaminated site has:
High metal concentrations- Metals that cannot be broken down include arsenic, cadmium, mercury, copper, chromium and zinc
Mercury is most toxic of heavy metals
High Chlorinated organic molecules- These are organic molecules that have multiple chlorine atoms attached to them
Inorganic salts- This includes substances such as sodium thiosulfate, sulfur dioxide, sodium metabisulfite, trimethylamine hydrochloride and ferric chloride

## Slide 12: ADVANTAGES OF BIOREMEDIATION
Bioremediation is a natural process
Cost-effective
Toxic chemicals are destroyed or removed from environment and not just merely separated
Low capital expenditure
Less energy is required as compared to other technologies
Less manual supervision

## Slide 13: DIS-ADVANTAGES OF BIOREMEDIATION
Bioremediation is slow and time consuming process
Heavy metals cannot be removed
In-situ bioremediation site must have soil with high permeability
It does not remove all quantities of contaminants
Substantial gaps exist in the understanding of microbial ecology, physiology and genetic expression and site engineering
Scientific base is required for rational designing of process and success

## Slide 14: BIO-AUGMENTATION
This technique involves the augmentation of contaminant sites with non-native microbes which include genetically engineered microbes to degrade the contaminants
This process is called as bio-augmentation
This technique could expand the range of possibilities for future bioremediation systems

## Slide 15: THANK YOU