## Slide 1: UNIT-II
LOGIC FAMILIES

## Slide 2: TYPES OF LOGIC FAMILY

## Slide 3: Emitter-Coupled Logic (ECL)
Non saturated digital logic family & Used in high speed circuits
Propagation rate as low as 1-2ns
Noise immunity and power dissipation is high compare of all logic families.
It is also called as current mode logic. The design of ECL circuit consists of transistors and resistors.
By preventing the transistor from entering into saturation, the high-speed operation is achieved in ECL logic family.
Very small voltage swing is necessary to switch between the two different voltage levels. This cannot be achieved in transistor-transistor logic, as the transistors enter into saturation mode, while in operation.
Emitter-coupled logic family offers an incredible propagation delay of 1ns.
The delay is more reduced in the latest ECL families.
Notes: ‹#›

## Slide 4: Inverter Circuit of Emitter Coupled Logic (ECL)

## Slide 5: ECL NOR / OR
The circuit has 2 outputs- inverting and non inverting output, input low is 3.6 V, input high is 4.4V.
When A=B=0, so Q1, Q2 are OFF, then Out1=High and Out2=Low.
When A=B=1, so Q1, Q2 are ON, then Out1= low and Out2=High.

## Slide 6: ECL (NOR/OR GATE)

## Slide 7: Integrated Injection Logic
Integrated injection logic (IIL, I2L, or I2L) is a class of digital circuits built with multiple collector bipolar junction transistors (BJT).
When introduced it had speed comparable to TTL yet was almost as low power as CMOS, making it ideal for use in VLSI (and larger) integrated circuits.
The gates can be made smaller with this logic family than with CMOS because complementary transistors are not needed.
Although the logic voltage levels are very close (High: 0.7V, Low: 0.2V), I2L has high noise immunity because it operates by current instead of voltage.
I2L was developed in 1971 by Siegfried K. Wiedmann and Horst H. Berger who originally called it merged-transistor logic (MTL).
A disadvantage of this logic family is that the gates draw power when not switching

## Slide 8: Operating Principles of I2L gates
Integrated Injection Logic Operation is explained as follows. To understand the working of a typical I2L gate, consider the figure, which consists of five transistors, connected as shown.
It can be seen that the base current IB1 of T1 is derived from +VCC through the input terminal B. The base-bias current IB3 of transistor T3 and the collector current IC1 of T1 are obtained from the collector current of transistor T2 whose injector (emitter) also is connected to +VCC.

## Slide 9
If IB1 is sufficient, the base-to-emitter voltage VBE1 of T1 will become the saturation base-emitter voltage VBES1 (= 0.8 volt), and in this condition, its collector-to-emitter voltage VCE1 will become saturation base-emitter voltage VCES1 (= 0.2 volt).
So, we find that T1 is in the ON-state and its output is at logic-0 level. Since VCES1 = 0.2 volt, the collector current IC2 of T2 will flow through the collector of T1 as IC1, and VBE3 of T3 = 0.2 V = VCES1.
This means that at this moment, T3 is OFF and its collector-emitter voltage VCE3 = 0.8 volt. Now, let the input voltage Vi = 0 V. This makes transistor T1 to be in OFF-state, and IC2 to flow through the base of T2.
Thus, VBE3 = VBES3 = 0.8 V. This makes VCE1 = VBES3 = logic 1, and VCE3 = VCES3 = logic 0.
Thus, the transistors perform inversion operation, with logic 0 = VCES = 0.2 V, and logic 1 = VBES = 0.8 V. The voltage swing of this gate, therefore, is Vswing=VBES – VCES = 0.8 – 0.2 = 0.6 volt
It can be seen that the logic swing of I2L gates is very low and this is a major defect of these gates.

## Slide 10: Advantages of I2L Gates
Since I2L gates are made up only of BJTs, they possess high speed of operation. Because only transistors are used for the construction, I2L gates have high packing density, and are hence suitable for construction of VLSI circuits.
· Very low power-supply requirement (1 volt) .
· Low power dissipation
.
· Number of processing steps required is small; hence cost per gate is low.
· Several functions are possible on the same chip.
· Using bipolar technology, it is possible to combine I2L gates with other logic families.

## Slide 11: Disadvantages of I2L Gates
Very low voltage swing (≈ 0.6 V); the swing is between VBES (0.8 V) and VCES (0.2 V).
· Lower packing density than NMOS.
· Lower noise margin.
· External resistance required for proper functioning.
· I2L technology, at present, is dormant.