## Slide 1: Unit 2
S-7 | SLO-1 | PMOS,NMOS
 | SLO-2 | CMOS Logic

## Slide 2: nMOS Transistor
Four terminals: gate, source, drain, body
Gate – oxide – body stack looks like a capacitor
  Gate and body are conductors
  SiO2 (oxide) is a very good insulator
  Called metal – oxide – semiconductor (MOS) capacitor
  Even though gate is
  no longer made of metal

## Slide 3: nMOS Operation
Body is usually tied to ground (0 V)
When the gate is at a low voltage:
  P-type body is at low voltage
  Source-body and drain-body diodes are OFF
  No current flows, transistor is OFF

## Slide 4: nMOS Operation Cont.
When the gate is at a high voltage:
  Positive charge on gate of MOS capacitor
  Negative charge attracted to body
  Inverts a channel under gate to n-type
  Now current can flow through n-type silicon from source through channel to drain, transistor is ON

## Slide 5: pMOS Transistor
Similar, but doping and voltages reversed
  Body tied to high voltage (VDD)
  Gate low: transistor ON
  Gate high: transistor OFF
  Bubble indicates inverted behavior

## Slide 6: Power Supply Voltage
GND = 0 V
In 1980’s, VDD = 5V
VDD has decreased in modern processes
  High VDD would damage modern tiny transistors
  Lower VDD saves power
VDD = 3.3, 2.5, 1.8, 1.5, 1.2, 1.0, …

## Slide 7: Transistors as Switches
We can view MOS transistors as electrically controlled switches
Voltage at gate controls path from source to drain

## Slide 8: Static States of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.

## Slide 9: Static States of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.

## Slide 10: Static States of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.

## Slide 11: Static States of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.

## Slide 12: Static States of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.

## Slide 13: Static States of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.

## Slide 14: Static States of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.

## Slide 15: Static States of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.

## Slide 16: Static States of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.

## Slide 17: Static Characteristics of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.
The capacitor charges through RonP , current exists only during charging, no dc current exists.

## Slide 18: Static Characteristics of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.
The capacitor charges through RonP , current exists only during charging, no dc current exists.

## Slide 19: Static Characteristics of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.
The capacitor charges through RonP , current exists only during charging, no dc current exists.

## Slide 20: Static Characteristics of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.
The capacitor charges through RonP , current exists only during charging, no dc current exists.

## Slide 21: Static Characteristics of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.
The capacitor charges through RonP , current exists only during charging, no dc current exists.

## Slide 22: Static Characteristics of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.
The capacitor charges through RonP , current exists only during charging, no dc current exists.

## Slide 23: Static Characteristics of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.
The capacitor charges through RonP , current exists only during charging, no dc current exists.

## Slide 24: Static Characteristics of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.
The capacitor charges through RonP , current exists only during charging, no dc current exists.

## Slide 25: Static Characteristics of the CMOS Inverter
The capacitor discharges through RonN , current exists only during discharge, no dc current exists.
The capacitor charges through RonP , current exists only during charging, no dc current exists.

## Slide 26: CMOS Inverter
0
A | Y
0 | 1
1 | 0
OFF
ON
1
ON
OFF

## Slide 27: CMOS Logic Design
The design of logic gates for CMOC inverter is different from the similar logic design for NMOS inverters that we considered earlier.
For NMOS gates, the logic involved only the switching transistor.
For CMOS, both transistors are involved, since the input affects both in symmetrical way.
Thus, for each logic input variable in CMOS gate there is one transistor in NMOS network and one transistor in PMOS network.
CMOS logic gate structure
NMOS logic gate structure
Load transistor

## Slide 28: CMOS NOR Gate
Reference Inverter
CMOS NOR 2 input gate
A

## Slide 29: CMOS NOR Gate
Reference Inverter
CMOS NOR 2 input gate
For the two input NOR gate, the NMOS portion of the gate is identical to the NMOS gate.
A

## Slide 30: CMOS NOR Gate
Reference Inverter
CMOS NOR 2 input gate
For the two input NOR gate, the NMOS portion of the gate is identical to the NMOS gate.
In the CMOS gate, we must ensure that static current path does not exist through the logic gate, and this requires switching also in the PMOS transistor network  2 PMOS transistors.
A

## Slide 31: CMOS NOR Gate
Reference Inverter
CMOS NOR 2 input gate
A=1
For the two input NOR gate, the NMOS portion of the gate is identical to the NMOS gate.
In the CMOS gate, we must ensure that static current path does not exist through the logic gate, and this requires switching also in the PMOS transistor network  2 PMOS transistors.
In the NMOS section, the conducting path exists for A=1 or B=1.
A
Y=0

## Slide 32: CMOS NOR Gate
Reference Inverter
CMOS NOR 2 input gate
A=1
For the two input NOR gate, the NMOS portion of the gate is identical to the NMOS gate.
In the CMOS gate, we must ensure that static current path does not exist through the logic gate, and this requires switching also in the PMOS transistor network  2 PMOS transistors.
In the NMOS section, the conducting path exists for A=1 or B=1.
A=1
B=1
A
Y=0
Y=0

## Slide 33: CMOS NOR Gate
Reference Inverter
CMOS NOR 2 input gate
A=0
A=1
For the two input NOR gate, the NMOS portion of the gate is identical to the NMOS gate.
In the CMOS gate, we must ensure that static current path does not exist through the logic gate, and this requires switching also in the PMOS transistor network  2 PMOS transistors.
In the NMOS section, the conducting path exists for A=1 or B=1.
In the PMOS section, the conducting path exists only when A=0 and B=0
A=1
B=1
A
Y=1
Y=0
Y=0

## Slide 34: CMOS NOR Gate
Reference Inverter
CMOS NOR 2 input gate
A=0
A=1
For the two input NOR gate, the NMOS portion of the gate is identical to the NMOS gate.
In the CMOS gate, we must ensure that static current path does not exist through the logic gate, and this requires switching also in the PMOS transistor network  2 PMOS transistors.
In the NMOS section, the conducting path exists for A=1 or B=1.
In the PMOS section, the conducting path exists only when A=0 and B=0
A=1
B=1
A=0 & B=0
A
Y=1
Y=0
Y=0
Y=1

## Slide 35: CMOS NOR Gate
Reference Inverter
CMOS NOR 2 input gate
A=0
A=1
For the two input NOR gate, the NMOS portion of the gate is identical to the NMOS gate.
In the CMOS gate, we must ensure that static current path does not exist through the logic gate, and this requires switching also in the PMOS transistor network  2 PMOS transistors.
In the NMOS section, the conducting path exists for A=1 or B=1.
In the PMOS section, the conducting path exists only when A=0 and B=0
Complimentary nature of conducting paths: for NMOS – parallel
A=1
B=1
A=0 & B=0
A
Y=1
Y=0
Y=0
Y=1

## Slide 36: CMOS NOR Gate
Reference Inverter
CMOS NOR 2 input gate
A
A=0
A=1
For the two input NOR gate, the NMOS portion of the gate is identical to the NMOS gate.
In the CMOS gate, we must ensure that static current path does not exist through the logic gate, and this requires switching also in the PMOS transistor network  2 PMOS transistors.
In the NMOS section, the conducting path exists for A=1 or B=1.
In the PMOS section, the conducting path exists only when A=0 and B=0
Complimentary nature of conducting paths: for NMOS – parallel, for PMOS - series
A=1
B=1
A=0 & B=0
Y=1
Y=0
Y=0
Y=1

## Slide 37: CMOS NOR Gate
Reference Inverter
CMOS NOR 2 input gate
CMOS NOR 3 input gate
A=0
A=1
For the two input NOR gate, the NMOS portion of the gate is identical to the NMOS gate.
In the CMOS gate, we must ensure that static current path does not exist through the logic gate, and this requires switching also in the PMOS transistor network  2 PMOS transistors.
In the NMOS section, the conducting path exists for A=1 or B=1.
In the PMOS section, the conducting path exists only when A=0 and B=0
Complimentary nature of conducting paths: for NMOS – parallel, for PMOS - series
A=1
B=1
A=0 & B=0
A
Y=1
Y=0
Y=0
Y=1

## Slide 38: CMOS NOR Gate
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 39: CMOS NAND Gates
CMOS NAND gate
Reference Inverter
A
Y

## Slide 40: CMOS NAND Gates
CMOS NAND gate
Reference Inverter
A=0
A=0
B=0
A
Y=1
Y
Y=1
Y=1

## Slide 41: CMOS NAND Gates
CMOS NAND gate
Reference Inverter
A=1
A=1 & B=1
A
Y=0
Y
Y=0

## Slide 42: CMOS NAND Gates
CMOS NAND gate
Reference Inverter
A=0
A=1
A=0
B=0
A=1 & B=1
A
Y=1
Y=0
Y
Y=1
Y=0
Y=1

## Slide 43: CMOS NAND Gates
CMOS NAND gate
Reference Inverter
A
Y
The same rules apply for sizing the NAND gate devices as for the NOR gate, except now the NMOS transistors are in series
(W/L)P will be the same size of that of the reference inverter

## Slide 44: CMOS NAND Gates
CMOS NAND gate
Reference Inverter
A
Y
The same rules apply for sizing the NAND gate devices as for the NOR gate, except now the NMOS transistors are in series
(W/L)P will be the same size of that of the reference inverter
(W/L)N will be twice the size of that of the reference inverter

## Slide 45: Multi-Input CMOS NAND Gates

## Slide 46: CMOS NAND Gate
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
OFF
OFF
ON
ON
1
1
OFF
ON
OFF
ON
0
1
ON
OFF
ON
OFF
1
0
ON
ON
OFF
OFF
0
0