## Slide 1: Unit - 3
Hardware Description Language

## Slide 2: Hardware Description Language - Introduction
HDL is a language that describes the hardware of digital systems in a textual form.
It resembles a programming language, but is specifically oriented to describing hardware structures and behaviors.
The main difference with the traditional programming languages is HDL’s representation of extensive parallel operations whereas traditional ones represents mostly serial operations.
The most common use of a HDL is to provide an alternative to schematics.

## Slide 3: HDL – Introduction
When a language is used for the above purpose (i.e. to provide an alternative to schematics), it is referred to as a structural description in which the language describes an interconnection of components.
Such a structural description can be used as input to logic simulation just as a schematic is used.
Models for each of the primitive components are required.
If an HDL is used, then these models can also be written in the HDL providing a more uniform, portable representation for simulation input.

## Slide 4: HDL – Introduction
HDL can be used to represent logic diagrams, Boolean expressions, and other more complex digital circuits.
Thus, in top down design, a very high-level description of a entire system can be precisely specified using an HDL.
This high-level description can then be refined and partitioned into lower-level descriptions as a part of the design process.

## Slide 5: HDL – Introduction
As a documentation language, HDL is used to represent and document digital systems in a form that can be read by both humans and computers and is suitable as an exchange language between designers.
The language content can be stored and retrieved easily and processed by computer software in an efficient manner.
There are two applications of HDL processing: Simulation and Synthesis

## Slide 6: Logic Simulation
A simulator interprets the HDL description and produces a readable output, such as a timing diagram, that predicts how the hardware will behave before its is actually fabricated.
Simulation allows the detection of functional errors in a design without having to physically create the circuit.

## Slide 7: Logic Simulation
The stimulus that tests the functionality of the design is called a test bench.
To simulate a digital system
  Design is first described in HDL
  Verified by simulating the design and checking it with a test bench which is also written in HDL.

## Slide 8: Logic Simulation
Logic simulation is a fast, accurate method of analyzing a circuit to see its waveforms

## Slide 9: Types of HDL
There are two standard HDL’s that are supported by IEEE.
  VHDL (Very-High-Speed Integrated Circuits Hardware Description Language) - Sometimes referred to as VHSIC HDL, this was developed from an initiative by US. Dept. of Defense.
  Verilog HDL – developed by Cadence Data systems and later transferred to a consortium called Open Verilog International (OVI).

## Slide 10: Verilog
Verilog HDL has a syntax that describes precisely the legal constructs that can be used in the language.
It uses about 100 keywords pre-defined, lowercase, identifiers that define the language constructs.
Example of keywords: module, endmodule, input, output wire, and, or, not , etc.,
Any text between two slashes (//) and the end of line is interpreted as a comment.
Blank spaces are ignored and names are case sensitive.

## Slide 11: Verilog Module
A module is the building block in Verilog.
It is declared by the keyword module and is always terminated by the keyword endmodule.
Each statement is terminated with a semicolon, but there is no semi-colon after endmodule.

## Slide 12: Verilog Module for simple circuit
HDL Example
    module smpl_circuit(A,B,C,x,y);
    input A,B,C;
    output x,y;
    wire e;
    and g1(e,A,B);
    not g2(y,C);
    or g3(x,e,y);
    endmodule

## Slide 13: Verilog – Gate Delays
Sometimes it is necessary to specify the amount of delay from the input to the output of gates.
In Verilog, the delay is specified in terms of time units and the symbol #.
The association of a time unit with physical time is made using timescale compiler directive.
Compiler directive starts with the “backquote (`)” symbol.
  `timescale 1ns/100ps
The first number specifies the unit of measurement for time delays.
The second number specifies the precision for which the delays are rounded off, in this case to 0.1ns.

## Slide 14: Verilog Module with Gate Delays
//Description of circuit with delay
module circuit_with_delay (A,B,C,x,y);
input A,B,C;
output x,y;
wire e;
and #(30) g1(e,A,B);
or #(20) g3(x,e,y);
not #(10) g2(y,C);
endmodule

## Slide 15: Test Bench
In order to simulate a circuit with HDL, it is necessary to apply inputs to the circuit for the simulator to generate an output response.
An HDL description that provides the stimulus to a design is called a test bench.
The initial statement specifies inputs between the keyword begin and end.
Initially ABC=000 (A,B and C are each set to 1’b0 (one binary digit with a value 0).
$finish is a system task.

## Slide 16: Test Bench for Simple Circuit
//Stimulus for simple circuit
module stimcrct;
reg A,B,C;
wire x,y;
circuit_with_delay cwd(A,B,C,x,y);
initial
begin
A = 1'b0; B = 1'b0; C = 1'b0;
#100
A = 1'b1; B = 1'b1; C = 1'b1;
#100 $finish;
end
endmodule
module circuit_with_delay (A,B,C,x,y);
input A,B,C;
output x,y;
wire e;
and #(30) g1(e,A,B);
or #(20) g3(x,e,y);
not #(10) g2(y,C);
endmodule

## Slide 17: Verilog Module for Boolean Expressions
Bitwise operators
  Bitwise NOT : ~
  Bitwise AND: &
  Bitwise OR: |
  Bitwise XOR: ^
  Bitwise XNOR: ~^ or ^~

## Slide 18: Verilog Module for Boolean Expressions
Boolean Expressions:
These are specified in Verilog HDL with a continuous assignment statement consisting of the keyword assign followed by a Boolean Expression.
The earlier circuit can be specified using the statement:
  assign x = (A&B)|~C)
  E.g. x = A + BC + B’D
  y = B’C + BC’D’

## Slide 19: Verilog Module for Boolean Expressions
//Circuit specified with Boolean equations
module circuit_bln (x,y,A,B,C,D);
input A,B,C,D;
output x,y;
assign x = A | (B & C) | (~B & C);
assign y = (~B & C) | (B & ~C & ~D);
endmodule

## Slide 20: User Defined Primitives
User Defined Primitives (UDP):
The logic gates used in HDL descriptions with keywords and, or,etc., are defined by the system and are referred to as system primitives.
The user can create additional primitives by defining them in tabular form.
These type of circuits are referred to as user-defined primitives.

## Slide 21: User Defined Primitives
UDP features ….
UDP’s do not use the keyword module. Instead they are declared with the keyword primitive.
There can be only one output and it must be listed first in the port list and declared with an output keyword.
There can be any number of inputs. The order in which they are listed in the input declaration must conform to the order in which they are given values in the table that follows.
The truth table is enclosed within the keywords table and endtable.
The values of the inputs are listed with a colon (:). The output is always the last entry in a row followed by a semicolon (;).
It ends with the keyword endprimitive.

## Slide 22: Verilog Module for User Defined Primitives
//User defined primitive(UDP)
primitive crctp (x,A,B,C);
output x;
input A,B,C;
//Truth table for x(A,B,C) = Minterms (0,2,4,6,7)
table
// A B C : x (Note that this is only a comment)
0 0 0 : 1;
0 0 1 : 0;
0 1 0 : 1;
0 1 1 : 0;
1 0 0 : 1;
1 0 1 : 0;
1 1 0 : 1;
1 1 1 : 1;
endtable
endprimitive
// Instantiate primitive
module declare_crctp;
reg x,y,z;
wire w;
crctp (w,x,y,z);
endmodule

## Slide 23: Types of Modeling
A module can be described in any one (or a combination) of the following modeling techniques.
  Gate-level modeling using instantiation of primitive gates and user defined modules.
    This describes the circuit by specifying the gates and how they are connected with each other.
  Dataflow modeling using continuous assignment statements with the keyword assign.
    This is mostly used for describing combinational circuits.
  Behavioral modeling using procedural assignment statements with keyword always.
    This is used to describe digital systems at a higher level of abstraction.

## Slide 24: Gate-Level Modeling
Here a circuit is specified by its logic gates and their interconnections.
It provides a textual description of a schematic diagram.
Verilog recognizes 12 basic gates as predefined primitives.
  4 primitive gates of 3-state type.
  Other 8 are: and, nand, or, nor, xor, xnor, not, buf
When the gates are simulated, the system assigns a four-valued logic set to each gate – 0,1,unknown (x) and high impedance (z)

## Slide 25: Gate-level modeling
When a primitive gate is incorporated into a module, we say it is instantiated in the module.
In general, component instantiations are statements that reference lower-level components in the design, essentially creating unique copies (or instances) of those components in the higher-level module.
Thus, a module that uses a gate in its description is said to instantiate the gate.

## Slide 26: Gate-level Modeling
Modeling with vector data (multiple bit widths):
  A vector is specified within square brackets and two numbers separated with a colon.
  e.g. output[0:3] D; - This declares an output vector D with 4 bits, 0 through 3.
  wire[7:0] SUM; – This declares a wire vector SUM with 8 bits numbered 7 through 0.
  The first number listed is the most significant bit of the vector.

## Slide 27: Gate-level Modeling
Two or more modules can be combined to build a hierarchical description of a design.
There are two basic types of design methodologies.
  Top down: In top-down design, the top level block is defined and then sub-blocks necessary to build the top level block are identified.
  Bottom up: Here the building blocks are first identified and then combine to build the top level block.
In a top-down design, a 4-bit binary adder is defined as top-level block with 4 full adder blocks. Then we describe two half-adders that are required to create the full adder.
In a bottom-up design, the half-adder is defined, then the full adder is constructed and the 4-bit adder is built from the full adders.

## Slide 28: Gate-level Modeling
A bottom-up hierarchical description of a 4-bit adder is described in Verilog as
  Half adder: defined by instantiating primitive gates.
  Then define the full adder by instantiating two half-adders.
  Finally the third module describes 4-bit adder by instantiating 4 full adders.
Note: In Verilog, one module definition cannot be placed within another module description.

## Slide 29: 4-bit Half Adder

## Slide 30
4-bit Full Adder

## Slide 31
//Gate-level hierarchical description of 4-bit adder
module halfadder (S,C,x,y);
input x,y;
output S,C;
//Instantiate primitive gates
xor (S,x,y);
and (C,x,y);
endmodule
module fulladder (S,C,x,y,z);
input x,y,z;
output S,C;
wire S1,D1,D2; //Outputs of first XOR and two AND gates
//Instantiate the half adders
halfadder HA1(S1,D1,x,y), HA2(S,D2,S1,z);
or g1(C,D2,D1);
endmodule
4-bit Full Adder

## Slide 32
module _4bit_adder (S,C4,A,B,C0);
input [3:0] A,B;
input C0;
output [3:0] S;
output C4;
wire C1,C2,C3; //Intermediate carries
//Instantiate the full adder
fulladder FA0 (S[0],C1,A[0],B[0],C0),
FA1 (S[1],C2,A[1],B[1],C1),
FA2 (S[2],C3,A[2],B[2],C2),
FA3 (S[3],C4,A[3],B[3],C3);
endmodule
4-bit Full Adder

## Slide 33: 2 to 4 Decoder

## Slide 34: 2 to 4 Decoder
//Gate-level description of a 2-to-4-line decoder
module decoder_gl (A,B,E,D);
input A,B,E;
output[0:3]D;
wire Anot,Bnot,Enot;
not
n1 (Anot,A),
n2 (Bnot,B),
n3 (Enot,E);
nand
n4 (D[0],Anot,Bnot,Enot),
n5 (D[1],Anot,B,Enot),
n6 (D[2],A,Bnot,Enot),
n7 (D[3],A,B,Enot);
endmodule

## Slide 35: 2-to-4 Line Decoder

## Slide 36: 2-to-4 Line Decoder
//2 to 4 line decoder
module decoder_2_to_4_st_v(E_n, A0, A1, D0_n, D1_n, D2_n, D3_n);
input E_n, A0, A1;
output D0_n, D1_n, D2_n, D3_n;
wire A0_n, A1_n, E;
not g0(A0_n, A0), g1(A1_n, A1), g2(E,E_n);
nand g3(D0_n,A0_n,A1_n,E), g4(D1_n,A0,A1_n,E),
g5(D2_n,A0_n,A1,E), g6(D3_n,A0,A1,E);
endmodule

## Slide 37: Dataflow Modeling
Dataflow modeling uses a number of operators that act on operands to produce desired results.
Verilog HDL provides about 30 operator types.
Dataflow modeling uses continuous assignments and the keyword assign.
A continuous assignment is a statement that assigns a value to a net.
The value assigned to the net is specified by an expression that uses operands and operators.

## Slide 38: Dataflow Modeling - 2-to-4-line decoder
//Dataflow description of a 2-to-4-line decoder
module decoder_df (A,B,E,D);
input A,B,E;
output [0:3] D;
assign D[0] = ~(~A & ~B & ~E),
D[1] = ~(~A & B & ~E),
D[2] = ~(A & ~B & ~E),
D[3] = ~(A & B & ~E);
endmodule
A 2-to-1 line multiplexer with data inputs A and B, select input S, and output Y is described with the continuous assignment
assign Y = (A & S) | (B & ~S)

## Slide 39: Dataflow Modeling - 4-bit adder and 4-bit comparator
//Dataflow description of 4-bit adder
module binary_adder (A,B,Cin,SUM,Cout);
input [3:0] A,B;
input Cin;
output [3:0] SUM;
output Cout;
assign {Cout,SUM} = A + B + Cin;
endmodule
//Dataflow description of a 4-bit comparator.
module magcomp (A,B,ALTB,AGTB,AEQB);
input [3:0] A,B;
output ALTB,AGTB,AEQB;
assign ALTB = (A < B),
AGTB = (A > B),
AEQB = (A == B);
endmodule

## Slide 40: Dataflow Modeling - 2-to-1-line mux
Dataflow Modeling provides the means of describing combinational circuits by their function rather than by their gate structure.
Conditional operator (?:)
  condition ? true-expression : false-expression;
A 2-to-1 line multiplexer
  assign OUT = select ? A : B;
//Dataflow description of 2-to-1-line mux
module mux2x1_df (A,B,select,OUT);
input A,B,select;
output OUT;
assign OUT = select ? A : B;
endmodule