## Slide 1: ANALOG AND DIGITAL ELECTRONICS
UNIT 3 – COMBINATIONAL LOGIC CIRCUITS
READ ONLY MEMORY
-S.Vaishali

## Slide 2: Read Only Memory (ROM)
Data stored in a ROM is non-volatile, i.e. this data is permanently stored until erased or changed through re-programming (if applicable)
The ROM has n input lines for the address and m output data lines
Total memory capacity of a ROM is 2n x m bits
ROMs do not have input lines as a write operation does not exist in them
Programmable ROMs receive data to be programmed on the output lines
Generally, system-level programs that need to be accessed frequently and at power up access are stored in the computer’s ROM, e.g. the BIOS firmware

## Slide 3: Read Only Memory (ROM) Programmable sum of (fixed) minterms
Example: 8 X 4 PROM (n = 3 input lines, m = 4 output lines)
The fixed "AND" array is a “decoder” with 3 inputs and 8 outputs implementing minterms
The programmable "OR“ array uses a single line to represent all inputs to an OR gate. An “X” in the array corresponds to attaching the minterm to the OR
Read Example: For input (A2,A1,A0) = 010, output is (F3,F2,F1,F0 ) = 1001.
What are functions F3, F2 , F1 and F0 in terms of (A2, A1, A0)?
D0
D1
D2
D3
D4
D5
D6
D7
A2
A1
A0
A
B
C
F0
F1
F2
F3
X
X
X
X
X
X
X
X
X
X
2n x m Programmable
Connections
8 X 3-input fixed ANDs give all 8 minterms
8 Minterms
m0
m7

## Slide 4: Read Only Memory (ROM): n i/ps to m o/ps 2n locations x m bits each
Read Only Memories (ROM) have:
  n input (address) lines 🡪 2n locations 🡪 2n decoded minterms
  m output lines (word width)
Fixed array of 2n AND gates implementing all the N-literal minterms.
Programmable OR Array with m outputs lines to form up to m expressions, each being a sum of selected minterm.
The program for a PROM is simply the multiple-output truth table to be implemented
  If a 1 entry, a connection is made to the corresponding minterm for the corresponding output
  If a 0, no connection is made
Can be viewed as a memory with the inputs as addresses of data (output values), hence ROM or PROM names! Device on previous slide is an 8 x 4 memory (8 locations, each 4 bits)
Truth table is a listing of the memory contents

## Slide 5: Read Only Memory (ROM) Advantages/Limitations
Advantages:
Can implement any function (all the minterms are available)
Program is derived directly from the truth table (uses the canonical form)
Disadvantages:
Becomes complex for a large number of inputs n (# of ANDs = 2n, each n-input wide)
Does not support multi-level circuits (no outputs brought back as inputs)

## Slide 6: Types of ROM Devices
Simply ROM: Programmed only once and by the manufacturer (in factory), based on the client’s truth table
PROM: A ROM programmable only once by the user (in the field). The user blows fuses to remove unwanted connections. This process is irreversible and hence device is programmed only once
EPROM: Erasable, Programmable ROMs. Can have their data erased using Ultraviolet light and reprogrammed. The user can then reprogram the ROM many times using special programmers Off- situ.
Off-situ: Remove from
computer to erase/program

## Slide 7: Types of ROM, Contd.
EEPROMs: Electrically Erasable Programmable ROMs. Have memory cells that can be erased and reprogrammed by exposure to electrical signals.
Erasure/Programming is now much easier and in-situ. The processor can now “write” into the EEPROM.
Flash memory devices:
  Memory cells are erased in blocks not one-by-one as in EEPROMs 🡪 Shorter life but faster operation