## Slide 1: DEMULTIPLEXER
PREPARED BY
Mr.P.KANAKARAJ
AP/EEE
SRMIST-KTR

## Slide 2: Demultiplexer:
It is a combinational logic circuit.
It is a circuit that receives information on a single line and transmits this information on one of 2n possible output lines.
The selection of specific output line is controlled by the values of n selection lines.
Input – 1
Output – 2n
Selection lines – n
De-Multiplexer – 1 : 2n
There is a Enable input, which is required to connect two or three multiplexer in parallel.
DEMUX
2n
Output Lines
1
Input Line
Enable Input
n
Selected Lines

## Slide 3: Design of 1:4 DEMUX:
Input: 1 (I )
Output: 4 (Y0, Y1, Y2 & Y3)
Selection Line: 2 (S0 & S1)
Outputs are,
Selection Lines |  | Outputs |  |  | 
0 | 0 | I | 0 | 0 | 0
0 | 1 | 0 | I | 0 | 0
1 | 0 | 0 | 0 | I | 0
1 | 1 | 0 | 0 | 0 | I
Selection Lines |  | Outputs |  |  | 
0 | 0 | I | 0 | 0 | 0
0 | 1 | 0 | I | 0 | 0
1 | 0 | 0 | 0 | I | 0
1 | 1 | 0 | 0 | 0 | I
Truth Table

## Slide 4
Outputs are,
Logic Diagram of 1:4 DEMUX:

## Slide 5
1:4
DEMUX
1:4 DEMUX

## Slide 6: Design of 1:8 DEMUX
Input: 1 (I )
Output: 8 (Y0, Y1, Y2, Y3, Y4, Y5, Y6, Y7)
Selection Line: 3 (S0, S1 & S2)
Outputs are,
Selection Lines |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | I | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | I | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | I | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | I | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | I | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | I | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | I | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | I
Selection Lines |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | I | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | I | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | I | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | I | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | I | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | I | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | I | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | I
Truth Table

## Slide 7
Outputs are,
Logic Diagram of 1:8 DEMUX:

## Slide 8: 1:8 DEMUX
1:8
DEMUX

## Slide 9: Design of 1:8 DEMUX Using 1:4 DEMUX
1:4
DEMUX
1:4
DEMUX
C
C
C
D
D
D
B

## Slide 10: Implementation of Full Adder using Demultiplexer
Decimal | Inputs |  |  | Outputs | 
 | A | B | C | Sum | Carry
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0
2 | 0 | 1 | 0 | 1 | 0
3 | 0 | 1 | 1 | 0 | 1
4 | 1 | 0 | 0 | 1 | 0
5 | 1 | 0 | 1 | 0 | 1
6 | 1 | 1 | 0 | 0 | 1
7 | 1 | 1 | 1 | 1 | 1
Truth Table
Output Expressions are,
Sum =
Carry =
1:8
DEMUX

## Slide 11: Implementation of Full Subtractor using Demultiplexer
Decimal | Inputs |  |  | Outputs | 
 | A | B | C | Difference | Borrow
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1
2 | 0 | 1 | 0 | 1 | 1
3 | 0 | 1 | 1 | 0 | 1
4 | 1 | 0 | 0 | 1 | 0
5 | 1 | 0 | 1 | 0 | 0
6 | 1 | 1 | 0 | 0 | 0
7 | 1 | 1 | 1 | 1 | 1
Truth Table
Output Expressions are,
Difference =
Borrow =
1:8
DEMUX

## Slide 12: Applications of Demultiplexer:
Clock demultiplexer
Security monitoring system
Synchronous data transmission system

## Slide 13: THANK YOU…

## Slide 14: ANY QUERIEES???…