## Slide 1: ENCODER
Prepared By
Mr.P.KANAKARAJ
AP/EEE
SRMIST-KTR

## Slide 2: Encoder:
It is a combinational logic circuit.
An encoder has 2n input lines and n output lines.
The n output lines generate the binary code for the possible 2n input lines.
Input – 2n
Output – n
Encoder – 2n : n
2n:n
Encoder
2n
Input Lines
n
Output Lines

## Slide 3: Four to Two Line Binary Encoder
Decimel Value | Input |  |  |  | Output | 
0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 1
2 | 0 | 1 | 0 | 0 | 1 | 0
3 | 1 | 0 | 0 | 0 | 1 | 1
Decimel Value | Input |  |  |  | Output | 
0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 1
2 | 0 | 1 | 0 | 0 | 1 | 0
3 | 1 | 0 | 0 | 0 | 1 | 1
Input – 4
Output – 2
Outputs are,
Truth Table

## Slide 4: Eight to Three Line Binary Encoder (Octal to Binary Encoder
Decimal Value | Input |  |  |  |  |  |  |  | Output |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
3 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
4 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
5 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
6 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
7 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
Decimal Value | Input |  |  |  |  |  |  |  | Output |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
3 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
4 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
5 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
6 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
7 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
Input – 8
Output – 3
Outputs are,
Truth Table

## Slide 5: Priority Encoder:
It is an encoder circuit that includes the priority function.
In that priority encoder, if two or more inputs are equal to 1 at the same time, the input having the highest priority will take precedence.
Input |  |  |  | Output |  | 
0 | 0 | 0 | 0 |  |  | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 0 | 1 | 1
 |  | 1 | 0 | 1 | 0 | 1
 |  |  | 1 | 1 | 1 | 1
Input |  |  |  | Output |  | 
0 | 0 | 0 | 0 |  |  | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 0 | 1 | 1
 |  | 1 | 0 | 1 | 0 | 1
 |  |  | 1 | 1 | 1 | 1
Truth Table
K-Map Simplification
 | 00 | 01 | 11 | 10
00 | X | 1 | 1 | 1
01 | 0 | 1 | 1 | 1
11 | 0 | 1 | 1 | 1
10 | 0 | 1 | 1 | 1
 | 00 | 01 | 11 | 10
00 | X | 1 | 1 | 0
01 | 1 | 1 | 1 | 0
11 | 1 | 1 | 1 | 0
10 | 0 | 1 | 1 | 0
 | 00 | 01 | 11 | 10
00 | 0 | 1 | 1 | 1
01 | 1 | 1 | 1 | 1
11 | 1 | 1 | 1 | 1
10 | 1 | 1 | 1 | 1

## Slide 6: Logic Diagram for Priority Encoder
Expressions are,

## Slide 7: THANK YOU…

## Slide 8: ANY QUERIEES???…