## Slide 1
Transistor Amplifier: CE amplifier
Transistor Amplifier: CB and CC amplifier
UNIT 1
Introduction to Analog Electronics
Session-3

## Slide 2: COMPARISON BETWEEN BJT AND JFET
BJT | JFET
Bipolar Device | Unipolar Device
Current Controlled Device | Voltage Controlled Device
Low Input Impedance | High Input Impedance
Consumes more power | Consumes less power
High Noise level | Low noise level
Low thermal stability | High thermal stability
Large size | Small size
Preferred in low current application | Preferred in low voltage application
High gain | Low – medium gain

## Slide 3: Transistor Amplifier
The transistor raises the strength of a weak signal and hence acts an amplifier
The transistor works as an amplifier in all configuration (CE, CB and CC)

## Slide 4: Transistor Amplifier: CE amplifier
npn transistor in CE mode
Input between Base and Emitter
Output between Collector and Emitter
Input current IB
Output current IC
Input junction (BE)-forward biased
Output junction (CE)-Reverse biased
The VBB battery provides the forward bias
The VCC battery provides the reverse bias
Notes: 1.npn transistor

## Slide 5: Write KVL in output circuit
Write KVL in Input circuit
VBB = IBRB+VBE

## Slide 6
Link between input and output current
IB increases IC increases
IB decreases IC decreases
Variation in collector current gives variation in output voltage
Transistor works as a amplifier in proper operating point
VBB+VI

## Slide 7
Load line
Each point of load line is the operating point of a transistor

## Slide 8: Amplifier
Capacitor connected to the input and output side remove DC component
IC increases : VCE voltage decreases
Voltage gain AV=VCE/VI

## Slide 9
Operation of Common Emitter Amplifier
  When a signal is applied across the emitter-base junction during the positive half cycle the forward bias across this junction increases.
  This increases the flow of electrons from the emitter to a collector through the base, thus increases the collector current.
  The increasing collector current induces more voltage drops across the collector load resistor RC.
  The negative half cycle decreases the forward bias voltage across the emitter-base junction.
  The decreasing collector-base voltage reduces the collector current in the whole collector resistor RC.
  Thus, the amplified load resistor appears across the collector resistor

## Slide 10
The emitter and base of the transistor are connected in forward biased and the collector base region is in reverse bias.
The input signal or weak signal is applied across the emitter base and the output is obtained to the load resistor RC which is connected in the collector circuit.
The DC voltage VEE is applied to the input circuit along with the input signal to achieve the amplification
Common Base Transistor as an Amplifier
When a weak signal is applied to the input, a small change in signal voltage causes a change in emitter current (or we can say a change of 0.1V in signal voltage causes a change of 1mA in the emitter current) because the input circuit has very low resistance.
This change is almost the same in collector current because of the transmitter action.
In the collector circuit, a load resistor RC of high value is connected.
When collector current flows through such a high resistance, it produces a large voltage drop across it.
Thus, a weak signal (0.1V) applied to the input circuit appears in the amplified form (10V) in the collector circuit.

## Slide 11
Common Base (CB) Amplifier
When positive half-cycle of the signal is applied, then
forward bias is decreased because VBE is already negative with respect to the ground
2. consequently, IB is decreased.
3. IE and hence IC are decreased
4. The drop IC RC is decreased.
5. Hence, VCB is increased
Since a positive-going input signal produces a positive-going output signal, there is no phase reversal
Voltage amplification in this circuit is possible by reason of relative input and output circuitry rather than current gain (α) which is always less than unity.
The input circuit has low resistance whereas output circuit has very large resistance.
Although changes in input and output currents are the same, the ac drop across RL is very large.
Hence, changes in VCB (which is the output voltage) are much larger than changes in input ac signal. Hence, the voltage amplification.

## Slide 12
Common Collector (CC) Amplifier
1. forward bias is increased since VBE is positive
w.r.t. collector i.e. ground,
2. base current is increased,
3. emitter current is increased,
4. drop across RE is increased,
5. hence, output voltage (i.e. drop across RE is
increased.
When a positive-going input signal results in a positive going output signal and, consequently, the input and output signals are in phase