## Slide 1: DECODER
PREPARED BY
Mr.P.KANAKARAJ
AP/EEE
SRMIST-KTR

## Slide 2: Decoder:
It is a combinational logic circuit.
It has an n-bit binary input code and a one activated output out of 2n output code is called binary decoder.
A binary decoder is used when it is necessary to activate exactly one of 2n outputs based on an n-bit input value.
It is similar to demultiplexer, with only one exception that it has no data input.
Input – n
Output – 2n
Decoder – n : 2n
There is a Enable input, which is required to connect two or three decoder in parallel.
DECODER
n:2n
2n
Output Lines
Enable Input
n
Input Lines

## Slide 3: Decoder Vs Demultiplexer
Decoder
  Decoder is a many inputs to many outputs device.
  There are no selection lines.
Demultiplexer
  Demultiplexer is a one input to many outputs device.
  The selection of specific output line is controlled by the value of selection lines.

## Slide 4: Design of 2:4 DECODER
Input: 1 (I )
Output: 4 (Y0, Y1, Y2 & Y3)
Selection Line: 2 (S0 & S1)
Outputs are,
Input |  |  | Output |  |  | 
1 | X | X | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1
Input |  |  | Output |  |  | 
1 | X | X | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1
Truth Table

## Slide 5
Outputs are,
Logic Diagram of 2:4 Decoder

## Slide 6
2 to 4
Decoder
2 to 4 Line Decoder

## Slide 7: Three to Eight line Decoder
Input: 3 (S0, S1 , S2 )
Output: 8 (Y0, Y1, Y2, Y3, Y4, Y5, Y6, Y7)
Outputs are,
Input |  |  | Output |  |  |  |  |  |  | 
0 | 0 | 0 | I | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | I | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | I | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | I | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | I | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | I | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | I | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | I
Input |  |  | Output |  |  |  |  |  |  | 
0 | 0 | 0 | I | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | I | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | I | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | I | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | I | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | I | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | I | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | I
Truth Table

## Slide 8
Outputs are,
Logic Diagram of 3 to 8 line Decoder

## Slide 9: 3 to 8 Line Decoder
3 to 8
Decoder

## Slide 10: Design of 3 to 8 line Decoder Using 2 to 4 line Decoder
2 to 4
Decoder
2 to 4
Decoder

## Slide 11: Implementation of Full Adder using Decoder
Decimal | Inputs |  |  | Outputs | 
 | A | B | C | Sum | Carry
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0
2 | 0 | 1 | 0 | 1 | 0
3 | 0 | 1 | 1 | 0 | 1
4 | 1 | 0 | 0 | 1 | 0
5 | 1 | 0 | 1 | 0 | 1
6 | 1 | 1 | 0 | 0 | 1
7 | 1 | 1 | 1 | 1 | 1
Truth Table
Output Expressions are,
Sum =
Carry =
3 to 8
Decoder

## Slide 12: Implementation of Full Subtractor using Demultiplexer
Decimal | Inputs |  |  | Outputs | 
 | A | B | C | Difference | Borrow
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1
2 | 0 | 1 | 0 | 1 | 1
3 | 0 | 1 | 1 | 0 | 1
4 | 1 | 0 | 0 | 1 | 0
5 | 1 | 0 | 1 | 0 | 0
6 | 1 | 1 | 0 | 0 | 0
7 | 1 | 1 | 1 | 1 | 1
Truth Table
Output Expressions are,
Difference =
Borrow =
3 to 8
Decoder

## Slide 13: Implementation of given Boolean function using Decoder
Given Expressions are,
3 to 8
Decoder

## Slide 14: Implementation of given Boolean function using Decoder
Given Expressions are,
3 to 8
Decoder

## Slide 15: Applications of Decoder
It can be used to implement combinational circuit
It can be used to convert BCD into 7-segment code
It is used in memories to select particular register

## Slide 16: THANK YOU…

## Slide 17: ANY QUERIEES???…