## Slide 1
CONVERSIONS DIGITAL to ANALOG SIGNALS D/A

## Slide 2: Introduction
To interface the digital and analog world, we need converters that can convert analog to digital (ADC) and vice-versa (DAC).
Analog Signals:
  Physical quantities are “continuous” infinite number of quantities over a given range of values.
  Examples: temperature, pressure, time, velocity, acceleration, fluid flow, etc
Digital Signals:
  Digital signals are those with discrete values and are represented by binary codes.
  Examples: digital audio, computer system signals, electronic music systems.
Notes: 2

## Slide 3: Interfacing
Interfacing is a process of making 2 or more devices or systems operationally compatible with each other so that they function together as required
  . . . Interfacing Analog and Digital Worlds . . .
  converting digital codes to analog quantities and vice versa
Analog World
Continuous values in a given range
Digital World
Discrete set of values
Interface
Circuit
Analog-to-digital conversion (ADC)
Digital-to-analog conversion (DAC)
Notes: 3

## Slide 4: Real World Interfacing
Examples:
  Electronic thermostat,
  CD player,
  Digital Audio Tape (DAT) Player/Recorder
Sample discrete points in an analog curve
Digital reproduction of the analog curve
DAC
ADC
00000
00011
01001
01100
01101
10000
10010
00100
00101
01110
10001
Notes: 4

## Slide 5: Types of DACs
Many types of DACs available.
Usually switches, resistors, and op-amps used to implement conversion
Two Types:
  Binary Weighted Resistor
  R-2R Ladder

## Slide 6: Digital-to-Analog (D/A) Conversion
D/A conversion is the process of taking a value represented in digital code and converting it to a voltage or current that is proportional to the digital value
For each digital input code, the output is a unique analog value
4-bit
D/A Converter
(DAC)
D
C
B
A
Digital Inputs
Vout
Analog Output, Vout = digital input x k
Example: If k=0.5, and DCBA=1011,
what is the value of Vout ?
Analog Output = 11 x 0.5 = 5.5V
Notes: 6

## Slide 7: Resolution & Full Scale Voltage
Resolution or step size of a DAC is the smallest change that can occur in the analog output as a result of a step change in the digital input (LSB weightage)
  Analog output = digital input x k,
  k = analog output/digital input, (resolution or step size)
Full scale output is the DAC output when digital input is at maximum value,
  E.g. a 4-bit DAC FS output = 11112k = 15k = 15 x step size
  For n-bit DAC, full scale output = (2n – 1)k
  Example: If step size, k of a 10-bit DAC is 0.05V, the full scale output voltage is ______________
1023 x 0.05 = 51.15V
Notes: 7

## Slide 8: Full Scale Voltage
Full-scale voltage is the output voltage of DAC when maximum value of the digital inputs are applied.
Refer to figure below, the full scale voltage (when input is 111) is 7V. Step size or resolution is _______
3-bit DAC
F S output = 7V
Vout
0V
7V (full scale voltage)
1V
C
B
A
Another example: What is the step size for a 4-bit DAC operating with a full scale voltage of 8V? _________
3-bit counter
clock
8  15 = 0.53 V
tc
tc
0
0
0
0
0
1
0
1
0
1
1
1
Resolution =
= 1 V
Volts
x
7
1
2
1
3
-
1 V
Notes: 8

## Slide 9: Percentage Resolution
Although resolution can be expressed as the amount of output voltage per step, it is useful to express it as a percentage of the full scale output
  % resolution = (step size)/(full scale value) x 100%
  = k/(2n – 1)k x 100%
  =
  E.g. % Resolution of a 10-bit DAC is (1/1023)x100%
  = 0.098%
Will % resolution change if the full scale voltage is changed? ___________________________
1
x 100%
x 100%
2n – 1
NO, it only depends on the DAC number of bits
Notes: 9

## Slide 10: DAC Circuitry
There are several methods and circuits for producing the DAC.
However it is not necessary to familiar with all the various circuit schemes because DAC ICs are available, which do not require any circuit knowledge
Instead it is important to know the significant performance characteristics for intelligent use of the DAC IC
Notes: 10

## Slide 11: 4-bit DAC with Binary Weighted Inputs
+
–
+Vs
-Vs
Rf
R0
V0
Digital input
D3D2D1D0
Vout
I = 0
Isum
If
Virtual ground
For each input data bit,
  Vn = VHI (usually +5V) when digital data input Dn = 1
  Vn = 0 V for Dn = 0, where n = 0 to 3
That is, Vn = VHI (5V) or 0V , when Dn = 1 or 0 respectively
R1
V1
R2
V2
R3
V3
I0
I1
I2
I3
D0
D1
D2
D3
If = Isum = I3 + I2 + I1 + I0
1
+5V
0
0 V
Example
0
1
+5V
0 V
0 - Vout = If x Rf
?
where I3 = V3/R3, I2 = V2/R2, I1 = V1/R1, I0 = V0/R0
Vout = - If x Rf
1 0 0 1
(LSB)
(MSB)
Notes: 11

## Slide 12
In DAC, for every input bit, the voltage is assumed as 0V (if bit is logic 0) and +5V (if bit is logic 1).
  Example: if bit D0 = 0, then the voltage V0 = 0V
  if bit D0 = 1, then the voltage V0 = +5V
  Thus voltage at input is either 0V or +5V.
The input resistors R0 to R3 contribute the binary weightages. The current or voltage contribution from the LSB branch, I0 is the least and MSB branch, I3 is the most. To achieve this,
R0 = 2R1, R1 = 2R2, R2 = 2R3
(RLSB has largest value while RMSB has least value)
4-bit DAC with Binary Weighted Inputs
Notes: 12

## Slide 13
The operational amplifier is the summing amplifier and produces an output that is the weighted sum of the input voltages.
Isum is the summation of all the currents in the resistors flowing through the feedback resistor Rf.
Vout = - Isum Rf = - (I3 + I2 + I1 + I0) Rf
=
V1
R1
V3
R3
V2
R2
V0
R0
- Rf (
+
+
+
)
4-bit DAC with Binary Weighted Inputs
Notes: 13

## Slide 14
Vout = - Isum Rf = - (I3 + I2 + I1 + I0) Rf
Vout =
  where V3, V2, V1, V0 is logic 0 (0V) or logic 1 (5V) for TTL
For binary weighted currents to flow into R0, R1, R2, R3,
R0 = LSB resistor, R1= , R2= , R3=
Therefore, Vout =
R0
4
R0
2
V1
R1
V3
R3
V2
R2
V0
R0
- Rf (
+
+
+
)
R0
8
- Rf (
2V1
R0
8V3
R0
4V2
R0
1V0
R0
+
+
+
)
4-bit DAC with Binary Weighted Inputs
Notes: 14

## Slide 15
Vout =
=
Step-size is found by setting data input to 00012
Vstep-size =
Percentage resolution =
- Rf (
2V1
R0
8V3
R0
4V2
R0
V0
R0
+
+
+
)
(8V3 + 4V2 + 2V1 + V0)
Rf
R0
  where Vn is 0 or 5 volts
5Rf
RLSB
1
(2n – 1)
X 100%
4-bit DAC with Binary Weighted Inputs
Notes: 15

## Slide 16: Full Scale Voltage
Method 1: Vout =
  Where V3 = V2 = V1 = V0 = 5V
Method 2:
  For full scale output set input D3D2D1D0= 11112 (1510)
  VFS = =
  = step size x maximum digital input value
  = step size x (2n – 1) where n = no of bits
15
5Rf
R0
(11112)
5Rf
R0
V1
R1
V3
R3
V2
R2
V0
R0
- Rf (
+
+
+
)
Notes: 16

## Slide 17: Example 1
A 5-bit binary weighted DAC is given in the next slide. Assuming the input voltage at each bit is either 0V or +5V for logic 0 and 1 respectively, calculate
  Step size or resolution
  Full scale output voltage, Vout
  Vout for binary code of 11010
  Binary input for Vout = - 0.75V
  Given that Rf = 10 KΩ, R4 (MSB) = 25 KΩ
Notes: 17

## Slide 18
+
–
+Vs
-Vs
Rf
R0
V0
Vout
R1
V1
R2
V2
R3
V3
D0
D1
D2
D3
R4
V4
D4
MSB
LSB
Remember:
R0 is resistor for LSB and has the largest value
Example 1
Notes: 18

## Slide 19
Step size
Step size =
R0 = 400 kΩ (R0 is LSB resistor)
step size = - 5 Rf / R0 = - 5x10/400 V = - 0.125V
50kΩ,
R3 =
Full Scale Output voltage
Data = 11111 for Vout(FS)
Vout(FS) = (25 – 1) x step size = - 31 x 0.125V = - 3.875V
For data input = 11010,
Vout = 110102 x step size = - 26 x 0.125V = - 3.25V
Binary input = Vout/step-size = (-0.75)/(-0.125) = 610 = 001102
5Rf
R0
Example 1
R1 = 200kΩ
R2 = 100kΩ,
Notes: 19

## Slide 20: Example 2
The analog output of a 5-bit DAC as shown below is connected to a Light Emitting Diode (LED) circuit through an inverting unity gain buffer, so that its voltage is used to light up the LED.
+
–
Rf
RA
Vout
RB
RC
RD
A
B
C
D
RE
E
Inverting
Buffer
LED
Circuit
Notes: 20

## Slide 21: Example 2 (con’t)
Given that RA is the LSB resistor (least weighted resistor) of the DAC having a value of 800 kΩ, write down the resistance values of all the DAC input resistors RB, RC, RD, and RE.
Given that the magnitude of the full scale output of the DAC Vout is -3.875V, calculate the value of the feedback resistor Rf. Assume that a logic “1” at the inputs of the DAC is +5V and a logic “0” is 0V.
If the LED requires at least Vout=-1.5V to turn ON and that it can withstand a forward voltage of -15V, determine the range of input binary codes to the DAC that are able to turn ON the LED.
Notes: 21

## Slide 22: Example 2 Solution
The LSB resistor, RA has the highest value (smallest input current contribution to summing amplifier).
RB = RA/2 = 800k/2 = 400 kΩ
RC = RB/2 or RA/4 = 200 kΩ
RD = RC/2 or RA/8 = 100 kΩ
RE = RD/2 or RA/16 = 50 kΩ
Notes: 22

## Slide 23: Example 2 Solution
Full scale voltage = - 3.875V
Step size = - 3.875/(25-1) = - 0.125V
Step size = - 5Rf /RA = -0.125
Therefore Rf = (0.125 x 800)/5 kΩ = 20kΩ
For Vout = -1.5V, binary input = -1.5/step-size
= 1.5/0.125 = 12 (or 011002)
-15V exceeds the full scale output of -3.875V
Input codes to turn LED on are from 12 to 31
or 011002 to 111112
Notes: 23

## Slide 24: Binary Weighted Resistor
Advantages
  Simple Construction/Analysis
  Fast Conversion
Disadvantages
  Requires large range of resistors (2000:1 for 12-bit DAC) with necessary high precision for low resistors
  Requires low switch resistances in transistors
  Can be expensive. Therefore, usually limited to 8-bit resolution.

## Slide 25: R-2R Ladder
Bit: 0 0 0 0
Each bit corresponds
to a switch:
If the bit is high,
the corresponding
switch is connected to
the inverting input of
the op-amp.
If the bit is low, the
corresponding switch
is connected to ground.
4-Bit Converter
Vout
Vref

## Slide 26: R-2R Ladder
Vref
V2
V1
V3
Ideal Op-amp
2R
2R
V3

## Slide 27: R-2R Ladder
Vref
V2
V1
V3
Vout
V2
V3
R
R
Likewise,
I

## Slide 28: R-2R Ladder
Vref
V2
V1
V3
Results:
Where b3 corresponds to bit 3,
b2 to bit 2, etc.
If bit n is set, bn=1
If bit n is clear, bn=0
Vout

## Slide 29: R-2R Ladder
For a 4-Bit R-2R Ladder
For general n-Bit R-2R Ladder or Binary Weighted Resister DAC

## Slide 30: Problem
If the reference voltage is 1 V, and if all switches are connected, the output current can be calculated as follows:
Output voltage

## Slide 31: Problem
What will be the analog equivalent of 1001 0001?
Vref = 5V

## Slide 32: R-2R Ladder
Advantages
  Only two resistor values (R and 2R)
  Does not require high precision resistors
Disadvantage
  Lower conversion speed than binary weighted DAC